# MIS 4523/Infrastructure			Exam a			December 8, 1998

4:30, Room 101 Adams Hall					Tuesday

Name  ________________________________________		Private Key  __________

Mark all answers that apply.  Add an explanation for any responses that you think you need one.

- In a TURING MACHINE

  - **The instruction set is the set of response functions that depend on current state and tape value

  - **A program is the initial contents of the tape

  - A state is: read,  write and then move left or right one space

  - **Memory corresponds to a tape

- CACHE is used to

  - Make RAM appear larger by swapping blocks in and out

  - **Make RAM appear faster by storing frequently used instructions in very fast memory

  - Store blocks that are being transferred from one device to another

  - Makes communication faster by handling data I/O functions

- A multiplexor (MUX) is needed in a memory chip because

  - Most memory chips store several bits for each address

  - The MUX separates input and output requests

  - **Chips use the same pins for both row and column addresses to save cost on the bus

  - The MUX provides the refresh for the flip-flop circuits

- FRAGMENTATION in a DASD refers to

  - **The number of sectors or blocks per track

  - The scattering of sectors for a dataset due to file updates and deletes over time

  - The process of breaking a program into fragments or pages for virtual memory applications

  - The ration of words per block in a program file

- A DEVICE DRIVER is

  - **A routine in the operating system that manages specific attached devices

  - A user program that manages individual devices

  - Responsible for processing error messages from I/O devices and fixing the problem if possible

  - A batch program that operates primarily to send data to I/O devices in a uniprogramming environment

- A multi-programming OPERATING SYSTEM

  - Does not need device drivers

  - Switches from program to program by swapping the entire contents of memory to DASD

  - **Restarts after an interrupt by storing the contents of the CPU registers for reinitialization

  - Is contained in firmware

- What are differences between voice and data circuits

  - Voice circuits have to be faster to avoid latency

  - Voice communications are analog from end to end and data is digital

  - **Voice circuits must limit latency

  - **Voice circuits do not perform error checks

- Contention in an Ethernet LAN refers to

  - ++Two nodes can transmit at the same time and interfere with each other

  - **Whichever node gets the network first can use it

  - The way that a node that has a multiple packets reserves the network

  - ++When a node detects a collision it continues transmitting to assure that all nodes detect contention

- Category 5 cable is

  - Fiber optic glass

  - Single cable copper

  - **8 wire copper

  - 5 wire copper

- Which of the following functions are handled at OSI layer 3

  - MAC addressing

  - **Network Addressing

  - Wiring standards

  - ++Error Checking

- 10BaseT is a communication standard that specifies:

  - 100 Megabits Per Second

  - Fiber Optic connectors

  - Multiple channels on the same connections

  - **Unshielded Twisted Pair wiring

- The ability of a product to be expanded to different size machines and still operate is

  - **Scalability

  - ++Interoperability

  - Buy-in

  - Message oriented coordination

- What is MIDDLEWARE?

  - Software that identifies network addresses and updates router tables

  - Programs that run backbone networks between LAN and WAN protocols

  - Programming languages such as C or JAVA that are used for servers in client/server systems

  - **Provides services to client/server applications that simplify programming of the interfaces

- LAYER 2 SWITCHES

  - **Read only the header of a message

  - Are appropriate for forwarding based on network addresses

  - Operate in software

  - **Maintain forwarding tables (e.g. routing tables)

- A single threaded software product

  - **Can support only one user at a time

  - Is well suited to being shared by several clients on a server

  - Tends to be very efficient because it uses remote procedure calls

  - **Needs one copy of the software for each user

- A reason for IT managers to determine the businesses basic strategy is

  - Most businesses do not know how to develop a strategy that takes advantage of technology

  - **The kind of infrastructure that a company will support is different for different strategies

  - Ignoring business strategy usually leads to outsourcing information services

  - **Infrastructure cannot usually be justified on the basis of a single project

- A company that seeks to add value by customizing products to suit buyer preference is following a

  - Niche Strategy

  - Technological Excellence Strategy

  - **Customer Focus Strategy

  - Low Cost Strategy

- Reach, Range and Response refer to

  - Latency, bandwidth and packet size

  - Basic parameters of a service level agreement

  - **Locations, application mix and communication requirements

  - Customer focus, required technical excellence and cost control

- Problems with effective security include

  - **Security is resisted by organizations since it reduces efficiency

  - There are no good encryption routines for communicating with external customers

  - **Internal and accidental violations are as costly as external threats

  - **Security must be balanced against risk or it is too costly

- A HOT SITE for disaster recovery is

  - A location that is at very high risk for security compromise

  - A location that would be very expensive (“hot”) if it were compromises

  - A site that supports Host Only Technology for access protection

  - **A location whose computers can take over if a disaster occurs

- Firewalls are a security tool that

  - Provide public keys to trusted partners

  - **Accept packets only from trusted sources

  - Duplicates data for recovery in case of a disaster

  - ++Provides user authentication based on the MAC address

- Users of an encryption system use a PUBLIC KEY to

  - Encode and decode messages

  - **Encode but not decode messages

  - Decode but not encode messages

  - Communicate to a trusted third party to obtain a message key

- PACKET SNIFFING in a network is

  - Using a firewall to keep out unwanted messages

  - Changing the source address in a message you send to pretend it comes from a second location

  - Using an encryption scheme to be certain that a password is still current

  - **Reading every packet on a network

- A GORILLA vendor is

  - A customer that can dictate the price of services he buys

  - **A vendor that has a controlling market share of a critical technology

  - A vendor of a new product that will demand industry acceptance

  - A vendor of an old product that has a large, but declining market share

- JOB SCHEDULING technology in a network

  - **Starts batch jobs when planned

  - Keeps track of what version of software each node supports

  - **Assures that jobs that depend on each other run to completion in the right order

  - Manages interrupts so that multiple jobs can be scheduled at once

- An AGENT is

  - **A program that runs on a remote machine and reports results back to the managing node

  - A program that checks each machine in a network to determine what programs it has loaded

  - An internal auditor specializing in information security

  - Software whose license lets it run on any station as long as no more than the licensed number of versions is running at once

- Which of the following are desirable properties of METRICS?

  - Focus on profit rather than cost

  - Vary from month to month to capture changing priorities

  - **Be used by the people who collect them

  - **Be auditable

- Which of the following normally indicate a winning technology?

  - First to market

  - Best in market

  - **Large market share

  - **Low cost