# MIS 4523/Infrastructure			Quiz 2a			October 28, 1998

300, Room 101 Adams Hall					Wednesday

Name  ________________________________________		Private Key  __________

Mark all answers that apply.  Add an explanation for any responses that you think you need one.

- Why is the Local Loop connections to homes and businesses analog instead of digital?

  - ** Existing phones and switches would all have to be converted to digital equipment.

  - Analog is faster

  - Analog is easier to amplify over copper wire

  - Digital connections would require fiber optic lines into homes

- What are differences between voice and data circuits

  - Voice circuits have to be faster to avoid latency

  - Voice communications are analog from end to end and data is digital

  - ** Voice circuits must limit latency

  - ** Voice circuits do not perform error checks

- Why would you choose a bus topology for a Token Ring LAN?

  - A bus does not require as much wiring.

  - Bus cards and switches are cheaper

  - Busses are easier to connect clients to

  - ** Token Ring does not run over a bus topology

- Contention in an Ethernet LAN refers to

  - Two nodes can transmit at the same time and interfere with each other

  - ** Whichever node gets the network first can use it

  - The way that a node that has a multiple packets reserves the network

  - When a node detects a collision it continues transmitting to assure that all nodes detect contention

- Token ring provides for

  - **  Priority packets

  - ** Equal access for each node

  - ** Message acknowledgement

  - Collision detection

- Hubs in a LAN

  - ** May be used to simplify attaching clients to the LAN

  - Are Layer 3 devices

  - Can convert from Ethernet to Token Ring

  - Can provide a collapsed backbone architecture

- A device that takes packets from several messages and intermixes them on one wire is a

  - ** Switch

  - ** Router

  - ** CSU/DSU

  - ** Multiplexer

- Category 5 cable is

  - Fiber optic glass

  - Single cable copper

  - ** 8 wire copper

  - 5 wire copper

- Which of the following use a bus topology

  - ** ATM

  - FDDI

  - ** Gigabit Ethernet

  - SNA

  - SONET

- Client/Server architecture refers to an architecture in which

  - Operations are controlled by a central server

  - Each node acts as both a client and a server

  - ** Some nodes are dedicated to providing information to the other nodes who process it

  - The network operating system is loaded on a single node that manages the communications

- Which of the following functions are handled at OSI layer 3

  - MAC addressing

  - ** Network Addressing

  - Wiring standards

  - ** Error Checking

- Which of the following is Layer 1 technology?

  - ** RJ45 connectors

  - Routers

  - Switches

  - ** Hubs

- What is the OSI Reference Model?

  - A proprietary network architecture

  - The design standards for the Internet

  - ** A description of general network in layers used to simplify understanding

  - A set of specific network standards that manufacturers must design to

- What is a MAC ADDRESS?

  - A network location such as an office drop physically wired into the network

  - A circuit route between one node and another established at setup time

  - An Internet address defined by the network administrator

  - ** A device ID number burned in by the manufacturer

- How does MANCHESTER ENCODING provide for self-clocking?

  - It uses start and stop bits before each byte to restart synchronization

  - ** It changes voltage at the middle of every bit sent

  - It refers to atomic clocks to synchronize each node in the network

  - ** It specifies the length of each packet so receivers can synchronize with the packet

- 10BaseT is a communication standard that specifies:

  - 100 Megabits Per Second

  - Fiber Optic connectors

  - Multiple channels on the same connections

  - ** Unshielded Twisted Pair wiring

- Examples of a NETWORK OPERATING SYSTEM are:

  - SONET

  - ** Windows NT

  - The Internet

  - ** UNIX

- The CLIENT PORTION of an Ethernet network operating system

  - Packetizes the messages

  - ** Redirects commands to the network or to the CPU

  - Provides message oriented management

  - Replaces the interrupt manager in the client operating system

- Which NETWORK OPERATING SYSTEM is showing the fastest growth

  - ** Windows NT

  - Novell NetWare

  - UNIX

  - MVS

- The ability of a product to work on any platform in a network is

  - Scalability

  - ** Interoperability

  - Buy-in

  - Message oriented coordination

- What is MIDDLEWARE?

  - Software that identifies network addresses and updates router tables

  - WAN software that converts from LAN protocols to wide area protocols like SONET

  - Front end tools that simplify user communication with client nodes

  - ** Provides services to client/server applications that simplify programming of the interfaces

- What is a THREAD in a server program?

  - ** A version of the application program that serves a particular client session

  - The circuit path between a server and a particular client

  - Thinnet fiber optic cabling between the server and the network router

  - The routing scheme for packets in a WAN

- What is a Remote Procedure Call (RPC)?

  - ** A subroutine or module on a server that is invoked by a client program

  - A thread established by a client contact

  - A middleware request for a client service

  - A server message

- Which of the following describe Messaging Middleware (MOM)?

  - Client requests services from the server and waits for a response

  - ** Client queues up responses and executes other functions while waiting for responses

  - ** Server maintains communication with the client by encapsulating responses in a package addressed to the client.

  - Programmers distribute applications by looking at single machine code and moving subroutines to the server as appropriate

- PACKET SWITCHED connections over a network:

  - Route all packets through the same nodes

  - ** Rout packets individually

  - Confirm delivery of packets

  - Deliver packets in the same order they were sent

- SWITCHES

  - ** Read only the header of a message

  - Are appropriate for forwarding based on network addresses

  - Operate in software

  - ++ Maintain forwarding tables (e.g. routing tables)

- Why is the choice of MIDDLEWARE difficult?

  - ** Middleware products do not all interoperate with all applications

  - Vendors like Oracle do not support middleware

  - Middleware does not work with TCP/IP

  - ** There are many different products with different specialized advantages

- What are key issues in Evaluating Technology?

  - ** Price

  - Technical excellence

  - ** Market share

  - First to market

- What are problems with OBJECT TECHNOLOGY?

  - ** Immature software products (inefficient and not scalable)

  - No established manufacturers support objects

  - No network middleware

  - ** No universally accepted design methodologies