## Slide 1: Boundary-Value and Eigenvalue Problems Chapter 27
An ODE is accompanied by auxiliary conditions. These conditions are used to evaluate the integral that result during the solution of the equation. An nth order equation requires n conditions.
If all conditions are specified at the same value of the independent variable, then we have an initial-value problem.
If the conditions are specified at different values of the independent variable, usually at extreme points or boundaries of a system, then we have a boundary-value problem.

## Slide 2
Figure 27.1

## Slide 3: General Methods for Boundary-value Problems
Figure 27.2

## Slide 4
Boundary Conditions
Analytical Solution:
(Heat transfer coefficient)

## Slide 5
The Shooting Method/
Converts the boundary value problem to initial-value problem. A trial-and-error approach is then implemented to solve the initial value approach.
For example, the 2nd order equation can be expressed as two first order ODEs:
An initial value is guessed, say z(0)=10.
The solution is then obtained by integrating the two 1st order ODEs simultaneously.

## Slide 6
Using a the RK method shown in class.

## Slide 7
Using Goal seek- one obtains
T(10)=200. for z(0)=18.11654

## Slide 8
Using a 4th order RK method with a step size of 2:
T(10)=168.3797.
This differs from T(10)=200. Therefore a new guess is made, z(0)=20 and the computation is performed again.
z(0)=20 T(10)=285.8980
Since the two sets of points, (z, T)1 and (z, T)2, are linearly related, a linear interpolation formula is used to compute the value of z(0) as 12.6907 to determine the correct solution.

## Slide 9
Figure 27.3

## Slide 10
Finite Differences Methods.
The most common alternatives to the shooting method.
Finite differences are substituted for the derivatives in the original equation.
Finite differences equation applies for each of the interior nodes. The first and last interior nodes, Ti-1 and Ti+1, respectively, are specified by the boundary conditions.
Thus, a linear equation transformed into a set of simultaneous algebraic equations can be solved efficiently.

## Slide 11: Tridiagonal Systems
A tridiagonal system has a bandwidth of 3:
An efficient LU decomposition method, called Thomas algorithm, can be used to solve such an equation. The algorithm consists of three steps: decomposition, forward and back substitution, and has all the advantages of LU decomposition.

## Slide 12: Thomas algorithm
New values of ek. e’k= ek/ fk-1
New values of fk. f’k= fk –e’k* gk-1
Forward substitution: r’k= rk –e’k* r’k-1
Backward substitution: xn=r’n/f’n; xk= r’k -gk*xk+1)/f’k