$ Generated by PRO/II Keyword Generation System <version 3.37 - 09-16-97>
$ Generated on: Sun May 30 15:15:40 1999
TITLE DATE=10/06/98
  TOLERANCE STREAM=0.001,,0.001
  SEQUENCE SIMSCI
  CALCULATION TRIALS=160, RECYCLE=ALL
COMPONENT DATA
  LIBID 1,BENZENE/2,H2/3,CH/4,METHANE
THERMODYNAMIC DATA
  METHOD SYSTEM=PR, SET=PR01, DEFAULT
  METHOD SYSTEM=GS, SET=GS01
  METHOD SYSTEM=GS, SET=GS02
STREAM DATA
  PROPERTY STREAM=BENZENE, TEMPERATURE=100, PRESSURE=14.696, PHASE=M, &
         RATE(LV)=561.457, COMPOSITION(M)=1,100
  PROPERTY STREAM=S9, TEMPERATURE=60.001, PRESSURE=14.696, PHASE=M, &
         RATE(GV)=600000, COMPOSITION(M)=2,97.5/4,2.5
  PROPERTY STREAM=HYDROGEN, TEMPERATURE=100, PRESSURE=514.7, &
         REFSTREAM=S9
RXDATA
  RXSET ID=CYCLOHEXANE
    REACTION ID=FORMATION
      STOICHIOMETRY 1,-1/2,-3/3,1
      HORX HEAT=-87, REFCOMP=1, REFTEMP=77, REFPHASE=V
UNIT OPERATIONS
  MIXER UID=M1
      FEED RECYCLE,BENZENE,HYDROGEN
      PRODUCT  M=S1
      OPERATION PRESSURE=515
  HX   UID=E1
      HOT  FEED=S4, M=S5, DP=5
      COLD FEED=S1, M=S2, DP=5
      CONFIGURE COUNTER
      OPER CTEMP=250
  HX   UID=E3
      HOT  FEED=S5, M=S6, DP=5
      UTILITY WATER, TIN=60.001, TEMPERATURE=90
      CONFIGURE COUNTER
      OPER HTEMP=120
  FLASH UID=F1, KPRINT
      FEED S6
      PRODUCT  V=S7, W=FEED
      ISO  TEMPERATURE=120
  SPLITTER UID=SP1
      FEED S7
      PRODUCT  M=S8, M=PURGE
      OPERATION OPTION=FILL
      SPEC STREAM=S8, RATE(LBM/H),TOTAL,DRY, DIVIDE, STREAM=S7, &
                 RATE(LBM/H),TOTAL,DRY, VALUE=0.8
  COMPRESSOR UID=C1
      FEED S8
      PRODUCT  M=RECYCLE
      OPERATION CALCULATION=ASME, PRES=514.7, EFF=80
  HX   UID=E2
      COLD FEED=S2, M=S3, DP=5
      UTILITY STEAM, PSAT=215
      CONFIGURE COUNTER
      OPER CTEMP=300
  CONREACTOR UID=R1
      FEED S3
      PRODUCT  M=S4
      OPERATION ISOTHERMAL, TEMPERATURE=435, DP=15
      RXCALCULATION MODEL=STOIC, XOPTION=STOP
      RXSTOIC RXSET=CYCLOHEXANE
      REACTION FORMATION
      BASE COMPONENT=1
      CONVERSION 0.95
  COLUMN UID=T1
      PARAMETER TRAY=30,IO=80
      FEED FEED,16
      PRODUCT  OVHD(M)=TOP, BTMS(M)=BOTTOM,370, SUPERSEDE=OFF
      CONDENSER TYPE=PART, PRESSURE=14.7
      DUTY 1,1/2,30
      PSPEC PTOP=14.7
      PRINT PROPTABLE=PART, DIAGRAM
      ESTIMATE MODEL=CONVENTIONAL, RRATIO=8
      SPEC RRATIO, VALUE=24
      SPEC STREAM=BOTTOM,FRACTION, COMP=3,DRY, VALUE=0.985
      VARY DUTY=1,2
      REBOILER TYPE=KETTLE
END


 SIMULATION SCIENCES INC.          R                                   PAGE H-1
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                              CALCULATION                              
                                        HISTORY                        10/06/98
 ==============================================================================
 
 *** PROBLEM SOLUTION BEGINS
     FEED FLASH    COMPLETE
       LOOP  1     BEGINS   - 'LOOP1       '
     UNIT    1     SOLVED   - 'M1          '
     UNIT    3     SOLVED   - 'E1          '
     UNIT    4     SOLVED   - 'E3          '
     UNIT    5     SOLVED   - 'F1          '
     UNIT    6     SOLVED   - 'SP1         '
     UNIT    7     SOLVED   - 'C1          '
     UNIT    8     SOLVED   - 'E2          '
     UNIT    2     SOLVED   - 'R1          '
       MAX ERRORS:  X=1.  (FEED)                 T=322.  (FEED)
                    P=1.  (FEED)
       LOOP  1 NOT SOLVED AFTER   1 TRIALS
     UNIT    1     SOLVED   - 'M1          '
     UNIT    3     SOLVED   - 'E1          '
     UNIT    4     SOLVED   - 'E3          '
     UNIT    5     SOLVED   - 'F1          '
     UNIT    6     SOLVED   - 'SP1         '
     UNIT    7     SOLVED   - 'C1          '
     UNIT    8     SOLVED   - 'E2          '
     UNIT    2     SOLVED   - 'R1          '
       MAX ERRORS:  X=-.000692  (S1)             T=.0212  (S5)
                    P=-2.95E-9  (S6)
       LOOP  1     SOLVED AFTER   2 TRIALS
             INNER  0 : E(ENTH+SPEC) = 6.807E-02
             CALCULATING NEW MATRIX
             INNER  1 : E(ENTH+SPEC) = 4.714E-02  ALPHA =   .2500
             INNER  2 : E(ENTH+SPEC) = 3.016E-02  ALPHA =   .2500
             INNER  3 : E(ENTH+SPEC) = 1.604E-02  ALPHA =  1.0000
             INNER  4 : E(ENTH+SPEC) = 5.002E-03  ALPHA =  1.0000
       ITER  1 E(K) = 2.508E-02 E(ENTH+SPEC) = 5.002E-03  E(SUM) = 3.497E-01
               DAMP = 1.000E+00
             INNER  0 : E(ENTH+SPEC) = 3.180E-03
             INNER  1 : E(ENTH+SPEC) = 3.147E-03  ALPHA =   .2500
             INNER  2 : E(ENTH+SPEC) = 5.709E-04  ALPHA =  1.0000
       ITER  2 E(K) = 1.618E-02 E(ENTH+SPEC) = 5.709E-04  E(SUM) = 2.274E-01
               DAMP = 1.000E+00
             INNER  0 : E(ENTH+SPEC) = 1.888E-03
             INNER  1 : E(ENTH+SPEC) = 1.688E-03  ALPHA =   .2500
             INNER  2 : E(ENTH+SPEC) = 1.442E-03  ALPHA =  1.0000
             INNER  3 : E(ENTH+SPEC) = 1.148E-03  ALPHA =  1.0000
             INNER  4 : E(ENTH+SPEC) = 3.051E-04  ALPHA =  1.0000
             INNER  5 : E(ENTH+SPEC) = 1.108E-04  ALPHA =  1.0000
             INNER  6 : E(ENTH+SPEC) = 1.639E-05  ALPHA =  1.0000
       ITER  3 E(K) = 7.186E-03 E(ENTH+SPEC) = 1.639E-05  E(SUM) = 9.006E-02
               DAMP = 1.000E+00
             INNER  0 : E(ENTH+SPEC) = 4.859E-04
             INNER  1 : E(ENTH+SPEC) = 3.623E-04  ALPHA =  1.0000
             INNER  2 : E(ENTH+SPEC) = 5.986E-05  ALPHA =  1.0000
             INNER  3 : E(ENTH+SPEC) = 2.323E-05  ALPHA =  1.0000
             INNER  4 : E(ENTH+SPEC) = 1.321E-05  ALPHA =  1.0000
       ITER  4 E(K) = 4.691E-03 E(ENTH+SPEC) = 1.321E-05  E(SUM) = 4.975E-02


 SIMULATION SCIENCES INC.          R                                   PAGE H-2
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                              CALCULATION                              
                                        HISTORY                        10/06/98
 ==============================================================================
 
               DAMP = 1.000E+00
             INNER  0 : E(ENTH+SPEC) = 5.344E-04
             INNER  1 : E(ENTH+SPEC) = 3.558E-04  ALPHA =  1.0000
             INNER  2 : E(ENTH+SPEC) = 1.351E-04  ALPHA =  1.0000
             INNER  3 : E(ENTH+SPEC) = 1.689E-05  ALPHA =  1.0000
       ITER  5 E(K) = 2.391E-03 E(ENTH+SPEC) = 1.689E-05  E(SUM) = 2.396E-02
               DAMP = 1.000E+00
             INNER  0 : E(ENTH+SPEC) = 2.174E-04
             INNER  1 : E(ENTH+SPEC) = 1.105E-04  ALPHA =  1.0000
             INNER  2 : E(ENTH+SPEC) = 3.358E-05  ALPHA =  1.0000
             INNER  3 : E(ENTH+SPEC) = 3.969E-06  ALPHA =  1.0000
       ITER  6 E(K) = 1.126E-03 E(ENTH+SPEC) = 3.969E-06  E(SUM) = 1.005E-02
               DAMP = 1.000E+00
             INNER  0 : E(ENTH+SPEC) = 8.585E-05
             INNER  1 : E(ENTH+SPEC) = 1.864E-05  ALPHA =  1.0000
       ITER  7 E(K) = 8.667E-04 E(ENTH+SPEC) = 1.864E-05  E(SUM) = 6.506E-03
     UNIT    9     SOLVED   - 'T1          '
 *** PROBLEM SOLUTION REACHED
  
 *** THIS RUN USED 203.00 PRO/II SIMULATION UNITS
  
 *** RUN STATISTICS
     STARTED    15:15:22 05/30/99          NO ERRORS
     FINISHED   15:15:30 05/30/99          NO WARNINGS
     RUN TIMES                             NO MESSAGES
       INTERACTIVE     0 MIN,   .00 SEC
       CALCULATIONS    0 MIN,  7.60 SEC
       TOTAL           0 MIN,  7.60 SEC


 SIMULATION SCIENCES INC.          R                                   PAGE I-1
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                                         INDEX                         10/06/98
 ==============================================================================
 
  PAGE    CONTENTS
 ------  ----------------------------------------------------------------
     1   COMPONENT DATA
     2   CALCULATION SEQUENCE AND RECYCLES
     3   FLASH DRUM SUMMARY
     4   MIXER SUMMARY
         SPLITTER SUMMARY
     5     UNIT 6, 'SP1'
         COMPRESSOR SUMMARY
     6     UNIT 7, 'C1'
         HEAT EXCHANGER SUMMARY
     7     UNIT 3, 'E1'
     8     UNIT 4, 'E3'
     9     UNIT 8, 'E2'
         COLUMN SUMMARY
    10     UNIT 9, 'T1'
    12       TOWER DIAGRAM
    13       TRAY RATES AND DENSITIES
         CONVERSION REACTOR SUMMARY
    15     UNIT 2, 'R1'
    16   STREAM MOLAR COMPONENT RATES
    18   STREAM SUMMARY


 SIMULATION SCIENCES INC.          R                                   PAGE P-1
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                                     COMPONENT DATA                    10/06/98
 ==============================================================================
 
         COMPONENT         COMP. TYPE      PHASE     MOL. WEIGHT      API
   ---------------------   -----------  -----------  -----------  -----------
     1  BENZENE                LIBRARY      VAP/LIQ       78.115       28.425
     2  H2                     LIBRARY      VAP/LIQ        2.016     1889.929
     3  CH                     LIBRARY      VAP/LIQ       84.163       49.117
     4  METHANE                LIBRARY      VAP/LIQ       16.043      340.167
 
         COMPONENT             NBP      CRIT. TEMP.  CRIT. PRES.  CRIT. VOLM.
                                F            F          PSIA      FT3/LB-MOL
   ---------------------   -----------  -----------  -----------  -----------
     1  BENZENE                176.180      553.010      714.222       4.1648
     2  H2                    -423.040     -399.820      188.108       1.0412
     3  CH                     177.332      536.540      590.776       4.9337
     4  METHANE               -258.682     -116.680      667.195       1.5858
 
         COMPONENT         ACEN. FACT.  HEAT FORM.     G FORM.
                                        BTU/LB-MOL   BTU/LB-MOL
   ---------------------   -----------  -----------  -----------
     1  BENZENE                 .20900     35663.28     55752.37
     2  H2                     -.22000          .00          .00
     3  CH                      .21000    -52935.51     13627.34
     4  METHANE                 .01040    -32066.21    -21726.14


 SIMULATION SCIENCES INC.          R                                   PAGE P-2
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                           CALCULATION SEQUENCE AND RECYCLES           10/06/98
 ==============================================================================
 
 CALCULATION SEQUENCE
 
  SEQ    UNIT ID     UNIT TYPE     SEQ    UNIT ID     UNIT TYPE
  ---  ------------  ----------    ---  ------------  ----------
    1  M1            MIXER           6  C1            COMPRESSOR
    2  E1            HX              7  E2            HX
    3  E3            HX              8  R1            CONV REAC
    4  F1            FLASH           9  T1            COLUMN
    5  SP1           SPLITTER
 
 
 RECYCLE LOOPS
 
  --------------- LOOPS ---------------- ------------ TEAR STREAMS ------------
       ID       FIRST UNIT   LAST UNIT        ID       FROM UNIT     TO UNIT
  ------------ ------------ ------------ ------------ ------------ ------------
  LOOP1        M1           R1           RECYCLE      C1           M1
                                         S4           R1           E1


 SIMULATION SCIENCES INC.          R                                   PAGE P-3
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                                   FLASH DRUM SUMMARY                  10/06/98
 ==============================================================================
 
 FLASH ID                             F1
       NAME
  
       FEEDS                          S6
 
       PRODUCTS VAPOR                 S7
                LIQUID              FEED
 
 TEMPERATURE, F                  120.000
 PRESSURE, PSIA                  480.000
 PRESSURE DROP, PSI                 .000
 MOLE FRAC VAPOR                  .84807
 MOLE FRAC LIQUID                 .15193
 DUTY, MM BTU/HR                  .00000
 FLASH TYPE                   ISOTHERMAL
 
 
 VAPOR-LIQUID COMPOSITIONS AND K-VALUES FOR UNIT 5, 'F1'
 
        COMPONENT         VAPOR       LIQUID     K-VALUE
   -------------------  ----------  ----------  ----------
     1  BENZENE         8.4490E-04      .04518  1.8700E-02
     2  H2                  .90487      .01261  7.1770E+01
     3  CH                  .01250      .93417  1.3384E-02
     4  METHANE             .08178      .00804  1.0168E+01


 SIMULATION SCIENCES INC.          R                                   PAGE P-4
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                                     MIXER SUMMARY                     10/06/98
 ==============================================================================
 
 MIXER ID                             M1
       NAME
  
       FEEDS                     RECYCLE
                                 BENZENE
                                HYDROGEN
 
       PRODUCTS MIXED                 S1
 
 TEMPERATURE, F                  107.473
 PRESSURE, PSIA                  515.000
 PRESSURE DROP, PSI             -500.304
 MOLE FRAC VAPOR                  .89526
 MOLE FRAC LIQUID                 .10474


 SIMULATION SCIENCES INC.          R                                   PAGE P-5
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                                    SPLITTER SUMMARY                   10/06/98
 ==============================================================================
 
                                 UNIT 6, 'SP1'
 
                   STREAM ID       FRACTION     ------------- RATES ----------
                                                  LB-MOL/HR           LB/HR
                  ------------    ----------    -------------       ----------
  FEED                      S7                       2226.737         9473.816
  
  PRODUCTS                  S8       .8000           1781.390         7579.005
                         PURGE       .2000            445.347         1894.751
  
  TEMPERATURE, F                  120.0000
  PRESSURE, PSIA                  480.0000
  PRESSURE DROP, PSIA                .0000
  
  MOLE FRAC VAPOR                   1.0000
  MOLE FRAC TOTAL LIQUID             .0000


 SIMULATION SCIENCES INC.          R                                   PAGE P-6
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                                   COMPRESSOR SUMMARY                  10/06/98
 ==============================================================================
 
                                  UNIT 7, 'C1'
 
 FEEDS                                S8
 
 PRODUCTS VAPOR                  RECYCLE
 
 
 OPERATING CONDITIONS
 
                                    INLET   ISENTROPIC       OUTLET
                              -----------  -----------  -----------
  TEMPERATURE, F                   120.00       131.09       133.82
  PRESSURE, PSIA                   480.00       514.70       514.70
  ENTHALPY, MM BTU/HR              3.1892       3.3347       3.3711
  ENTROPY, BTU/LB-MOL-F           28.5061      28.5061      28.5406
  CP, BTU/LB-MOL-F                 7.4406                    7.4695
  CV, BTU/LB-MOL-F                 5.3802                    5.4079
  CP/(CP-R)                        1.3641                    1.3621
  CP/CV                            1.3829                    1.3812
  MOLE PERCENT VAPOR             100.0000     100.0000     100.0000
  MOLE PERCENT LIQUID               .0000        .0000        .0000
  ACT VAP RATE, M FT3/MIN           .3873
  ADIABATIC EFF, PERCENT                                    80.0000
  POLYTROPIC EFF, PERCENT                                   80.1877
  ISENTROPIC COEFFICIENT, K                                  1.3942
  POLYTROPIC COEFFICIENT, N                                  1.5376
  ASME "F" FACTOR                                            1.0000
  HEAD, FT
          ADIABATIC                                        14935.31
          POLYTROPIC                                       14970.36
          ACTUAL                                           18669.14
  WORK, HP
          THEORETICAL                                         57.19
          POLYTROPIC                                          57.32
          ACTUAL                                              71.49
 
  NOTE: POLYTROPIC AND ISENTROPIC COEFFICIENTS
        CALCULATED FROM ASME EQUATIONS


 SIMULATION SCIENCES INC.          R                                   PAGE P-7
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                                 HEAT EXCHANGER SUMMARY                10/06/98
 ==============================================================================
 
                                  UNIT 3, 'E1'
 
 OPERATING CONDITIONS
 
      DUTY, MM BTU/HR                           9.517
      LMTD, F                                 150.056
      F FACTOR (FT)                              .713
      MTD, F                                  107.034
      U*A, BTU/HR-F                         88911.801
 
 
 HOT SIDE CONDITIONS                            INLET       OUTLET
                                          -----------  -----------
      FEED                                         S4
      MIXED PRODUCT                                             S5
       VAPOR, LB-MOL/HR                      2625.667     2386.698
              M LB/HR                          42.308       22.725
          CP, BTU/LB-F                           .836         .988
      LIQUID, LB-MOL/HR                                    238.969
              M LB/HR                                       19.583
          CP, BTU/LB-F                                        .522
       TOTAL, LB-MOL/HR                      2625.667     2625.667
              M LB/HR                          42.308       42.308
      CONDENSATION, LB-MOL/HR                              238.969
       TEMPERATURE, F                         435.000      227.289
       PRESSURE, PSIA                         490.000      485.000
 
 
 COLD SIDE CONDITIONS                           INLET       OUTLET
                                          -----------  -----------
      FEED                                         S1
      MIXED PRODUCT                                             S2
       VAPOR, LB-MOL/HR                      3365.385     3725.529
              M LB/HR                          11.815       39.719
          CP, BTU/LB-F                          2.058         .871
      LIQUID, LB-MOL/HR                       393.720       33.576
              M LB/HR                          30.488        2.584
          CP, BTU/LB-F                           .378         .464
       TOTAL, LB-MOL/HR                      3759.105     3759.105
              M LB/HR                          42.303       42.303
      VAPORIZATION, LB-MOL/HR                              360.145
       TEMPERATURE, F                         107.473      250.000
       PRESSURE, PSIA                         515.000      510.000


 SIMULATION SCIENCES INC.          R                                   PAGE P-8
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                                 HEAT EXCHANGER SUMMARY                10/06/98
 ==============================================================================
 
                                  UNIT 4, 'E3'
 
 OPERATING CONDITIONS
 
      DUTY, MM BTU/HR                           5.337
      LMTD, F                                  93.372
      F FACTOR (FT)                              .933
      MTD, F                                   87.079
      U*A, BTU/HR-F                         61287.032
 
 
 HOT SIDE CONDITIONS                            INLET       OUTLET
                                          -----------  -----------
      FEED                                         S5
      MIXED PRODUCT                                             S6
       VAPOR, LB-MOL/HR                      2386.698     2226.737
              M LB/HR                          22.725        9.474
          CP, BTU/LB-F                           .988        1.749
      LIQUID, LB-MOL/HR                       238.969      398.930
              M LB/HR                          19.583       32.834
          CP, BTU/LB-F                           .522         .438
       TOTAL, LB-MOL/HR                      2625.667     2625.667
              M LB/HR                          42.308       42.308
      CONDENSATION, LB-MOL/HR                              159.961
       TEMPERATURE, F                         227.289      120.000
       PRESSURE, PSIA                         485.000      480.000
 
 COLD SIDE CONDITIONS                           INLET       OUTLET
                                          -----------  -----------
      COOLING WATER, LB/HR                 177898.322   177898.322
      TEMPERATURE, F                           60.001       90.000


 SIMULATION SCIENCES INC.          R                                   PAGE P-9
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                                 HEAT EXCHANGER SUMMARY                10/06/98
 ==============================================================================
 
                                  UNIT 8, 'E2'
 
 OPERATING CONDITIONS
 
      DUTY, MM BTU/HR                           2.176
      LMTD, F                                 111.294
      F FACTOR (FT)                             1.000
      MTD, F                                  111.294
      U*A, BTU/HR-F                         19550.058
 
 HOT SIDE CONDITIONS                            INLET       OUTLET
                                          -----------  -----------
      STEAM, LB-MOL/HR                        144.116      144.116
      SATURATION PRESSURE, PSIA               215.000
      SATURATION TEMPERATURE, F               388.160
 
 
 COLD SIDE CONDITIONS                           INLET       OUTLET
                                          -----------  -----------
      FEED                                         S2
      VAPOR PRODUCT                                             S3
       VAPOR, LB-MOL/HR                      3725.529     3759.105
              M LB/HR                          39.719       42.303
          CP, BTU/LB-F                           .871         .857
      LIQUID, LB-MOL/HR                        33.576
              M LB/HR                           2.584
          CP, BTU/LB-F                           .464
       TOTAL, LB-MOL/HR                      3759.105     3759.105
              M LB/HR                          42.303       42.303
      VAPORIZATION, LB-MOL/HR                               33.576
       TEMPERATURE, F                         250.000      300.000
       PRESSURE, PSIA                         510.000      505.000


 SIMULATION SCIENCES INC.          R                                  PAGE P-10
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                                     COLUMN SUMMARY                    10/06/98
 ==============================================================================
 
                                  UNIT 9, 'T1'
 
 TOTAL NUMBER OF ITERATIONS
 
     IN/OUT METHOD      7
 
 
 COLUMN SUMMARY
 
                            ---------- NET FLOW RATES -----------     HEATER
   TRAY    TEMP   PRESSURE   LIQUID    VAPOR    FEED     PRODUCT      DUTIES
           DEG F    PSIA                 LB-MOL/HR                  MM BTU/HR
  ------  ------- --------  -------- -------- --------- ---------  ------------
       1C   155.5    14.70     867.1                        36.1V      -11.5029
       2    170.5    14.70     904.0    903.3
       3    170.7    14.70     904.3    940.1
       4    170.9    14.70     904.4    940.4
       5    171.2    14.70     904.5    940.5
       6    171.4    14.70     904.4    940.6
       7    171.8    14.70     904.3    940.5
       8    172.2    14.70     904.1    940.4
       9    172.6    14.70     903.9    940.2
      10    173.0    14.70     903.7    940.0
      11    173.4    14.70     903.5    939.8
      12    173.8    14.70     903.4    939.6
      13    174.1    14.70     903.3    939.5
      14    174.4    14.70     903.2    939.4
      15    174.7    14.70     903.1    939.3
      16    174.8    14.70    1354.5    939.3    398.9M
      17    175.4    14.70    1356.9    991.7
      18    175.5    14.70    1356.8    994.1
      19    175.6    14.70    1356.6    994.0
      20    175.6    14.70    1356.6    993.9
      21    175.7    14.70    1356.7    993.8
      22    175.8    14.70    1356.8    993.9
      23    175.8    14.70    1356.9    994.0
      24    175.9    14.70    1356.8    994.1
      25    176.0    14.70    1356.7    994.0
      26    176.1    14.70    1356.6    993.9
      27    176.2    14.70    1356.5    993.8
      28    176.3    14.70    1356.6    993.7
      29    176.4    14.70    1356.6    993.8
      30R   176.5    14.70              993.8              362.8L       12.6446


 SIMULATION SCIENCES INC.          R                                  PAGE P-11
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                                     COLUMN SUMMARY                    10/06/98
 ==============================================================================
 
                              UNIT 9, 'T1'  (CONT)
 
 FEED AND PRODUCT STREAMS
 
  TYPE     STREAM    PHASE   FROM  TO   LIQUID        FLOW RATES    HEAT RATES
                             TRAY TRAY   FRAC         LB-MOL/HR     MM BTU/HR
  ----- ------------ ------  ---- ----  ------       ------------  ------------
  FEED  FEED         MIXED          16   .9692             398.93        1.3831
  PROD  TOP          VAPOR      1                           36.13         .5065
  PROD  BOTTOM       LIQUID    30                          362.80        2.0169
 
  OVERALL MOLE BALANCE, (FEEDS - PRODUCTS)             5.5072E-13
  OVERALL HEAT BALANCE, (H(IN) - H(OUT)  )                           1.4652E-03
 
 
 SPECIFICATIONS
 
      PARAMETER      TRAY   COMP   SPECIFICATION  SPECIFIED   CALCULATED
        TYPE          NO     NO        TYPE         VALUE       VALUE
  -----------------  ----  ------  -------------  ----------  ----------
  UNIT T1               1              RRATIO      2.400E+01   2.400E+01
  STRM BOTTOM          30       3  MOL FRACTION    9.850E-01   9.850E-01
 
 
 REFLUX RATIOS
 
                                     -------- REFLUX RATIOS --------
                                       MOLAR      WEIGHT   STD L VOL
                                     ---------  ---------  ---------
  REFLUX / FEED STREAM FEED             2.1737     2.1532     2.0499
  REFLUX / VAPOR DISTILLATE            23.9981    30.2998    27.9839


 SIMULATION SCIENCES INC.                                R                                                                PAGE P-12
 PROJECT                                           PRO/II  VERSION 5.0 ELEC V5.4                                             386/EM
 PROBLEM                                                       OUTPUT                                                              
                                                           COLUMN SUMMARY                                                  10/06/98
 ==================================================================================================================================
 
                                                        UNIT 9, 'T1'  (CONT)
 
  
 TOWER CONFIGURATION AND PROFILES


 +-------------FEED--------------+                                                               +---PRODUCTS/PUMPAROUNDS-+
      RATE      TEMP  HEAT CONTENT      VAPOR     TEMP   TRAY   PRES      LIQUID      HEAT EXCH       RATE     HEAT CONTENT
  M LB-MOL/HR   DEG F  MM BTU/HR     M LB-MOL/HR  DEG F  NUMBER PSIA   M LB-MOL/HR    MM BTU/HR   M LB-MOL/HR   MM BTU/HR 
 -------------  ----- ------------  ------------- -----  ------ ----- -------------   ---------- ------------- ------------
                                   ------------------------------------------------
                                   I                                              I
                                   I                                              I
                                   I                                              +-->               .0361V           .5065
                                   I    .0361                                     I
                                   I-----------   155.5  --1--   14.70  ----------+<--  -11.5029
                                   I                                        .8671 I
                                   I                                              I
                                   I    .9033                                     I
                                   I-----------   170.5  --2--   14.70  ----------I
                                   I                                        .9040 I
                                   I                                              I
                                   I    .9401                                     I
                                   I-----------   170.7  --3--   14.70  ----------I
                                   I                                        .9043 I
                                   I                                              I
                                   I    .9404                                     I
                                   I-----------   170.9  --4--   14.70  ----------I
                                   I                                        .9044 I
                                   I                                              I
                                   I    .9405                                     I
                                   I-----------   171.2  --5--   14.70  ----------I
                                   I                                        .9045 I
                                   I                                              I
                                   I    .9406                                     I
                                   I-----------   171.4  --6--   14.70  ----------I
                                   I                                        .9044 I
                                   I                                              I
                                   I    .9405                                     I
                                   I-----------   171.8  --7--   14.70  ----------I
                                   I                                        .9043 I
                                   I                                              I
                                   I    .9404                                     I
                                   I-----------   172.2  --8--   14.70  ----------I
                                   I                                        .9041 I
                                   I                                              I
                                   I    .9402                                     I
                                   I-----------   172.6  --9--   14.70  ----------I
                                   I                                        .9039 I
                                   I                                              I
                                   I    .9400                                     I
                                   I-----------   173.0  -10--   14.70  ----------I
                                   I                                        .9037 I
                                   I                                              I
                                   I    .9398                                     I
                                   I-----------   173.4  -11--   14.70  ----------I
                                   I                                        .9035 I
                                   I                                              I
                                   I    .9396                                     I
                                   I-----------   173.8  -12--   14.70  ----------I
                                   I                                        .9034 I
                                   I                                              I
                                   I    .9395                                     I
                                   I-----------   174.1  -13--   14.70  ----------I
                                   I                                        .9033 I
                                   I                                              I
                                   I    .9394                                     I
                                   I-----------   174.4  -14--   14.70  ----------I
                                   I                                        .9032 I
                                   I                                              I
                                   I    .9393                                     I
                                   I-----------   174.7  -15--   14.70  ----------I
                                   I                                        .9031 I
                                   I                                              I
     .3989M     119.1   1.3831  -->+                                              I
                                   I    .9393                                     I
                                   I-----------   174.8  -16--   14.70  ----------I
                                   I                                       1.3545 I
                                   I                                              I
                                   I    .9917                                     I
                                   I-----------   175.4  -17--   14.70  ----------I
                                   I                                       1.3569 I
                                   I                                              I
                                   I    .9941                                     I
                                   I-----------   175.5  -18--   14.70  ----------I
                                   I                                       1.3568 I
                                   I                                              I
                                   I    .9940                                     I
                                   I-----------   175.6  -19--   14.70  ----------I
                                   I                                       1.3566 I
                                   I                                              I
                                   I    .9939                                     I
                                   I-----------   175.6  -20--   14.70  ----------I
                                   I                                       1.3566 I
                                   I                                              I
                                   I    .9938                                     I
                                   I-----------   175.7  -21--   14.70  ----------I
                                   I                                       1.3567 I
                                   I                                              I
                                   I    .9939                                     I
                                   I-----------   175.8  -22--   14.70  ----------I
                                   I                                       1.3568 I
                                   I                                              I
                                   I    .9940                                     I
                                   I-----------   175.8  -23--   14.70  ----------I
                                   I                                       1.3569 I
                                   I                                              I
                                   I    .9941                                     I
                                   I-----------   175.9  -24--   14.70  ----------I
                                   I                                       1.3568 I
                                   I                                              I
                                   I    .9940                                     I
                                   I-----------   176.0  -25--   14.70  ----------I
                                   I                                       1.3567 I
                                   I                                              I
                                   I    .9939                                     I
                                   I-----------   176.1  -26--   14.70  ----------I
                                   I                                       1.3566 I
                                   I                                              I
                                   I    .9938                                     I
                                   I-----------   176.2  -27--   14.70  ----------I
                                   I                                       1.3565 I
                                   I                                              I
                                   I    .9937                                     I
                                   I-----------   176.3  -28--   14.70  ----------I
                                   I                                       1.3566 I
                                   I                                              I
                                   I    .9938                                     I
                                   I-----------   176.4  -29--   14.70  ----------I
                                   I                                       1.3566 I
                                   I                                              I
                                   I    .9938                                     I
                                   I-----------   176.5  -30--   14.70  ----------+<--   12.6446
                                   I                                        .3628 I
                                   I                                              +-->               .3628L          2.0169
                                   I                                              I
                                   I                                              I
                                   ------------------------------------------------


 SIMULATION SCIENCES INC.          R                                  PAGE P-13
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                                     COLUMN SUMMARY                    10/06/98
 ==============================================================================
 
                              UNIT 9, 'T1'  (CONT)
 
 TRAY NET VAPOR RATES AND DENSITIES
 
                                          --------------- RATES ---------------
  TRAY     MW     ACTUAL DENS   Z FROM                  STANDARD      ACTUAL
                     LB/FT3     DENSITY     M LB/HR     M FT3/HR     M FT3/HR
  ----  --------  ------------  --------  -----------  -----------  -----------
     1    64.574        .14689    .97877        2.333       13.712       15.884
     2    80.852        .18149    .96828       73.032      342.778      402.399
     3    81.032        .18186    .96816       76.178      356.750      418.866
     4    81.183        .18217    .96805       76.345      356.871      419.086
     5    81.351        .18250    .96794       76.514      356.922      419.255
     6    81.533        .18285    .96781       76.689      356.939      419.417
     7    81.724        .18320    .96768       76.865      356.921      419.571
     8    81.920        .18355    .96755       77.039      356.872      419.719
     9    82.113        .18388    .96743       77.205      356.804      419.861
    10    82.296        .18419    .96731       77.361      356.725      419.999
    11    82.463        .18447    .96720       77.501      356.648      420.132
    12    82.611        .18471    .96710       77.625      356.580      420.260
    13    82.737        .18491    .96702       77.731      356.525      420.379
    14    82.841        .18507    .96695       77.820      356.483      420.486
    15    82.925        .18520    .96690       77.892      356.452      420.579
    16    82.992        .18531    .96685       77.951      356.431      420.658
    17    83.677        .18675    .96636       82.979      376.317      444.322
    18    83.697        .18679    .96635       83.202      377.238      445.441
    19    83.718        .18682    .96633       83.216      377.209      445.441
    20    83.740        .18685    .96632       83.225      377.150      445.407
    21    83.764        .18689    .96630       83.244      377.127      445.420
    22    83.789        .18693    .96628       83.275      377.157      445.498
    23    83.816        .18697    .96627       83.313      377.206      445.601
    24    83.844        .18701    .96625       83.346      377.231      445.678
    25    83.874        .18705    .96623       83.372      377.212      445.706
    26    83.905        .18710    .96621       83.392      377.166      445.705
    27    83.937        .18715    .96619       83.415      377.126      445.713
    28    83.970        .18720    .96616       83.445      377.111      445.752
    29    84.004        .18725    .96614       83.479      377.115      445.815
    30    84.038        .18730    .96612       83.513      377.116      445.876


 SIMULATION SCIENCES INC.          R                                  PAGE P-14
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                                     COLUMN SUMMARY                    10/06/98
 ==============================================================================
 
                              UNIT 9, 'T1'  (CONT)
 
 TRAY NET LIQUID RATES AND DENSITIES
 
                                          --------------- RATES ---------------
  TRAY     MW     ACTUAL DENS   Z FROM                   STD LIQ      ACTUAL
                     LB/FT3     DENSITY     M LB/HR      FT3/HR       GAL/MIN
  ----  --------  ------------  --------  -----------  -----------  -----------
     1    81.530        48.214    .00377       70.698     1378.580      182.816
     2    81.690        47.566    .00373       73.844     1443.682      193.554
     3    81.847        47.411    .00375       74.012     1451.389      194.627
     4    82.021        47.241    .00377       74.181     1459.606      195.770
     5    82.210        47.058    .00379       74.355     1468.358      196.995
     6    82.409        46.866    .00382       74.532     1477.434      198.274
     7    82.613        46.670    .00384       74.706     1486.574      199.570
     8    82.814        46.477    .00386       74.872     1495.485      200.843
     9    83.004        46.295    .00388       75.027     1503.884      202.052
    10    83.179        46.129    .00390       75.168     1511.536      203.161
    11    83.332        45.982    .00392       75.292     1518.280      204.145
    12    83.463        45.857    .00394       75.398     1524.042      204.990
    13    83.572        45.753    .00395       75.487     1528.830      205.696
    14    83.659        45.670    .00396       75.559     1532.715      206.271
    15    83.729        45.603    .00396       75.617     1535.804      206.730
    16    83.783        45.552    .00397      113.480     2307.036      310.595
    17    83.798        45.520    .00397      113.703     2312.130      311.425
    18    83.813        45.505    .00397      113.717     2313.035      311.562
    19    83.829        45.490    .00397      113.726     2313.882      311.692
    20    83.846        45.473    .00398      113.745     2314.975      311.857
    21    83.865        45.455    .00398      113.776     2316.385      312.065
    22    83.884        45.437    .00398      113.814     2317.959      312.297
    23    83.905        45.417    .00398      113.847     2319.497      312.526
    24    83.927        45.396    .00398      113.873     2320.911      312.739
    25    83.950        45.374    .00399      113.893     2322.267      312.945
    26    83.973        45.352    .00399      113.916     2323.705      313.164
    27    83.997        45.329    .00399      113.946     2325.305      313.405
    28    84.022        45.305    .00399      113.980     2327.021      313.663
    29    84.047        45.281    .00400      114.015     2328.751      313.924
    30    84.072        45.257    .00400       30.501      623.263       84.025


 SIMULATION SCIENCES INC.          R                                  PAGE P-15
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                               CONVERSION REACTOR SUMMARY              10/06/98
 ==============================================================================
 
                                  UNIT 2, 'R1'
 
 OPERATING CONDITIONS
 
  REACTOR TYPE                                               ISOTHERMAL REACTOR
  DUTY, MM BTU/HR                                                      -29.4606
  TOTAL HEAT OF REACTION AT 77.00 F, MM BTU/HR                         -32.9049
 
                                 INLET                    OUTLET
                              -----------               -----------
  FEED                                 S3
  VAPOR  PRODUCT                                                 S4
  TEMPERATURE, F                   300.00                    435.00
  PRESSURE, PSIA                 505.0000                  490.0000
 
 
 REACTION DATA
 
                              --------- RATES, LB-MOL/HR ----------    FRACTION
       COMPONENT                  FEED        CHANGE      PRODUCT     CONVERTED
  ------------------          -----------  -----------  ----------- -----------
    1 BENZENE                    398.1237    -378.2175      19.9062       .9500
    2 H2                        3153.4961   -1134.6525    2018.8435       .3598
    3 CH                          22.2731     378.2175     400.4906
    4 METHANE                    185.2121        .0000     185.2121
 
      TOTAL                     3759.1049   -1134.6525    2624.4524
 
                                            LB-MOL/HR               FRACTION
    BASE COMPONENT              REACTION    CONVERTED              CONVERTED(1)
  ------------------          -----------  -----------             ------------
    1 BENZENE                      1          378.2175                    .9500
 
  (1) FRACTION CONVERTED BASED ON AMOUNT IN FEED
 
 
 REACTOR MASS BALANCE
 
                              ----------- RATES, LB/HR ------------    FRACTION
     COMPONENT                    FEED        CHANGE      PRODUCT     CONVERTED
  ------------------          -----------  -----------  ----------- -----------
    1 BENZENE                  31099.4319  -29544.4603    1554.9716       .9500
    2 H2                        6357.4482   -2287.4596    4069.9886       .3598
    3 CH                        1874.5692   31831.9214   33706.4906
    4 METHANE                   2971.3573        .0000    2971.3573
 
      TOTAL                    42302.8065        .0000   42302.8080


 SIMULATION SCIENCES INC.          R                                  PAGE P-16
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                              STREAM MOLAR COMPONENT RATES             10/06/98
 ==============================================================================
 
 STREAM ID                       BENZENE       BOTTOM         FEED     HYDROGEN
        NAME
        PHASE                     LIQUID       LIQUID       LIQUID        VAPOR
  
 FLUID RATES, LB-MOL/HR
    1  BENZENE                  396.6186       5.4428      18.0249        .0000
    2  H2                          .0000        .0000       5.0297    1541.5693
    3  CH                          .0000     357.3532     372.6666        .0000
    4  METHANE                     .0000        .0000       3.2085      39.5274
 
 TOTAL RATE, LB-MOL/HR          396.6186     362.7960     398.9298    1581.0967
 
 TEMPERATURE, F                 100.0000     176.4757     120.0000      99.9999
 PRESSURE, PSIA                  14.6959      14.7000     480.0000     514.6960
 ENTHALPY, MM BTU/HR               .9892       2.0169       1.3831       2.2575
 MOLECULAR WEIGHT                78.1150      84.0723      82.3062       2.3667
 MOLE FRAC VAPOR                   .0000        .0000        .0000       1.0000
 MOLE FRAC LIQUID                 1.0000       1.0000       1.0000        .0000
 
 
 STREAM ID                         PURGE      RECYCLE           S1           S2
        NAME
        PHASE                      VAPOR        VAPOR        MIXED        MIXED
  
 FLUID RATES, LB-MOL/HR
    1  BENZENE                     .3763       1.5051     398.1237     398.1237
    2  H2                       402.9817    1611.9268    3153.4961    3153.4961
    3  CH                         5.5683      22.2731      22.2731      22.2731
    4  METHANE                   36.4212     145.6847     185.2121     185.2121
 
 TOTAL RATE, LB-MOL/HR          445.3474    1781.3897    3759.1049    3759.1049
 
 TEMPERATURE, F                 120.0000     133.8215     107.4732     250.0000
 PRESSURE, PSIA                 480.0000     514.7000     515.0000     510.0000
 ENTHALPY, MM BTU/HR               .7973       3.3711       6.6178      16.1344
 MOLECULAR WEIGHT                 4.2545       4.2545      11.2534      11.2534
 MOLE FRAC VAPOR                  1.0000       1.0000        .8953        .9911
 MOLE FRAC LIQUID                  .0000        .0000        .1047   8.9318E-03


 SIMULATION SCIENCES INC.          R                                  PAGE P-17
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                              STREAM MOLAR COMPONENT RATES             10/06/98
 ==============================================================================
 
 STREAM ID                            S3           S4           S5           S6
        NAME
        PHASE                      VAPOR        VAPOR        MIXED        MIXED
  
 FLUID RATES, LB-MOL/HR
    1  BENZENE                  398.1237      19.9062      19.9062      19.9062
    2  H2                      3153.4961    2018.8435    2019.9392    2019.9392
    3  CH                        22.2731     400.4906     400.5069     400.5069
    4  METHANE                  185.2121     185.2121     185.3145     185.3145
 
 TOTAL RATE, LB-MOL/HR         3759.1049    2624.4524    2625.6668    2625.6668
 
 TEMPERATURE, F                 300.0000     435.0000     227.2889     120.0000
 PRESSURE, PSIA                 505.0000     490.0000     485.0000     480.0000
 ENTHALPY, MM BTU/HR             18.3102      20.2179      10.7064       5.3696
 MOLECULAR WEIGHT                11.2534      16.1187      16.1133      16.1133
 MOLE FRAC VAPOR                  1.0000       1.0000        .9090        .8481
 MOLE FRAC LIQUID                  .0000        .0000        .0910        .1519
 
 
 STREAM ID                            S7           S8           S9          TOP
        NAME
        PHASE                      VAPOR        VAPOR        VAPOR        VAPOR
  
 FLUID RATES, LB-MOL/HR
    1  BENZENE                    1.8814       1.5051        .0000      12.5821
    2  H2                      2014.9085    1611.9268    1541.5693       5.0297
    3  CH                        27.8414      22.2731        .0000      15.3135
    4  METHANE                  182.1058     145.6847      39.5274       3.2085
 
 TOTAL RATE, LB-MOL/HR         2226.7371    1781.3897    1581.0967      36.1338
 
 TEMPERATURE, F                 120.0000     120.0000      60.0000     155.5411
 PRESSURE, PSIA                 480.0000     480.0000      14.6959      14.7000
 ENTHALPY, MM BTU/HR              3.9865       3.1892       1.8281        .5065
 MOLECULAR WEIGHT                 4.2545       4.2545       2.3667      64.5738
 MOLE FRAC VAPOR                  1.0000       1.0000       1.0000       1.0000
 MOLE FRAC LIQUID                  .0000        .0000        .0000        .0000


 SIMULATION SCIENCES INC.          R                                  PAGE P-18
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                                     STREAM SUMMARY                    10/06/98
 ==============================================================================
 
 STREAM ID                       BENZENE       BOTTOM         FEED     HYDROGEN
        NAME
        PHASE                     LIQUID       LIQUID       LIQUID        VAPOR
  
 -----  TOTAL STREAM  -----
 RATE, LB-MOL/HR                 396.619      362.796      398.930     1581.097
       M LB/HR                    30.982       30.501       32.834        3.742
 STD LIQ RATE, FT3/HR            561.456      623.263      672.527      745.768
 TEMPERATURE, F                  100.000      176.476      120.000      100.000
 PRESSURE, PSIA                   14.696       14.700      480.000      514.696
 MOLECULAR WEIGHT                 78.115       84.072       82.306        2.367
 ENTHALPY, MM BTU/HR                .989        2.017        1.383        2.257
           BTU/LB                 31.929       66.124       42.124      603.288
 MOLE FRACTION LIQUID             1.0000       1.0000       1.0000        .0000
 REDUCED TEMP (KAYS RULE)          .5527        .6384        .5916       8.3622
         PRES (KAYS RULE)          .0206        .0248        .8110       2.5724
 ACENTRIC FACTOR                   .2090        .2100        .2029       -.2142
 WATSON K (UOPK)                   9.719       10.965       10.953       42.713
 STD LIQ DENSITY, LB/FT3          55.181       48.937       48.822        5.018
         SPECIFIC GRAVITY          .8848        .7847        .7828        .0805
         API GRAVITY              28.425       48.829       49.254     1627.294
 
 --------  VAPOR  ---------
 RATE, LB-MOL/HR                     N/A          N/A          N/A     1581.097
       M LB/HR                       N/A          N/A          N/A        3.742
       M FT3/HR                      N/A          N/A          N/A       18.634
 STD VAP RATE(1), M FT3/HR           N/A          N/A          N/A      600.000
 SPECIFIC GRAVITY (AIR=1.0)          N/A          N/A          N/A    8.171E-02
 MOLECULAR WEIGHT                    N/A          N/A          N/A        2.367
 ENTHALPY, BTU/LB                    N/A          N/A          N/A      603.288
 CP, BTU/LB-F                        N/A          N/A          N/A        2.963
 DENSITY, LB/M FT3                   N/A          N/A          N/A      200.814
 Z (FROM DENSITY)                    N/A          N/A          N/A       1.0099
 
 --------  LIQUID  --------
 RATE, LB-MOL/HR                 396.619      362.796      398.930          N/A
       M LB/HR                    30.982       30.501       32.834          N/A
       FT3/HR                    575.119      673.954      696.163          N/A
       GAL/MIN                    71.703       84.025       86.794          N/A
 STD LIQ RATE, FT3/HR            561.456      623.263      672.527          N/A
 SPECIFIC GRAVITY (H2O=1.0)        .8848        .7847        .7828          N/A
 MOLECULAR WEIGHT                 78.115       84.072       82.306          N/A
 ENTHALPY, BTU/LB                 31.929       66.124       42.124          N/A
 CP, BTU/LB-F                       .371         .483         .438          N/A
 DENSITY, LB/FT3                  53.870       45.257       47.165          N/A
 Z (FROM DENSITY)             3.5480E-03   4.0001E-03        .1347          N/A
 
  (1) STANDARD VAPOR VOLUME IS 379.49 FT3/LB-MOLE (60 F AND 14.696 PSIA)


 SIMULATION SCIENCES INC.          R                                  PAGE P-19
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                                     STREAM SUMMARY                    10/06/98
 ==============================================================================
 
 STREAM ID                         PURGE      RECYCLE           S1           S2
        NAME
        PHASE                      VAPOR        VAPOR        MIXED        MIXED
  
 -----  TOTAL STREAM  -----
 RATE, LB-MOL/HR                 445.347     1781.390     3759.105     3759.105
       M LB/HR                     1.895        7.579       42.284       42.284
 STD LIQ RATE, FT3/HR            227.445      909.782     2216.791     2216.791
 TEMPERATURE, F                  120.000      133.821      107.473      250.000
 PRESSURE, PSIA                  480.000      514.700      515.000      510.000
 MOLECULAR WEIGHT                  4.255        4.255       11.248       11.248
 ENTHALPY, MM BTU/HR                .797        3.371        6.618       16.134
           BTU/LB                420.793      444.792      156.510      381.575
 MOLE FRACTION LIQUID              .0000        .0000        .1047   8.9318E-03
 REDUCED TEMP (KAYS RULE)         6.0687       6.2134       3.1473       3.9382
         PRES (KAYS RULE)         2.0621       2.2112       1.9089       1.8903
 ACENTRIC FACTOR                  -.1954       -.1954       -.1607       -.1607
 WATSON K (UOPK)                  29.231       29.231       16.133       16.133
 STD LIQ DENSITY, LB/FT3           8.331        8.331       19.074       19.074
         SPECIFIC GRAVITY          .1336        .1336        .3058        .3058
         API GRAVITY             927.828      927.828      331.158      331.158
 
 --------  VAPOR  ---------
 RATE, LB-MOL/HR                 445.347     1781.390     3365.385     3725.529
       M LB/HR                     1.895        7.579       11.817       39.721
       M FT3/HR                    5.810       22.209       40.105       55.638
 STD VAP RATE(1), M FT3/HR       169.002      676.008     1277.108     1413.777
 SPECIFIC GRAVITY (AIR=1.0)         .147         .147         .121         .368
 MOLECULAR WEIGHT                  4.255        4.255        3.511       10.662
 ENTHALPY, BTU/LB                420.793      444.792      464.731      399.879
 CP, BTU/LB-F                      1.749        1.756        2.058         .871
 DENSITY, LB/M FT3               326.121      341.266      294.647      713.921
 Z (FROM DENSITY)                 1.0066       1.0075       1.0084       1.0001
 
 --------  LIQUID  --------
 RATE, LB-MOL/HR                     N/A          N/A      393.720       33.576
       M LB/HR                       N/A          N/A       30.488        2.584
       FT3/HR                        N/A          N/A      573.484       54.142
       GAL/MIN                       N/A          N/A       71.499        6.750
 STD LIQ RATE, FT3/HR                N/A          N/A      558.989       47.398
 SPECIFIC GRAVITY (H2O=1.0)          N/A          N/A        .8745        .8741
 MOLECULAR WEIGHT                    N/A          N/A       77.435       76.961
 ENTHALPY, BTU/LB                    N/A          N/A       36.938       97.055
 CP, BTU/LB-F                        N/A          N/A         .378         .464
 DENSITY, LB/FT3                     N/A          N/A       53.162       47.726
 Z (FROM DENSITY)                    N/A          N/A        .1232        .1080
 
  (1) STANDARD VAPOR VOLUME IS 379.49 FT3/LB-MOLE (60 F AND 14.696 PSIA)


 SIMULATION SCIENCES INC.          R                                  PAGE P-20
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                                     STREAM SUMMARY                    10/06/98
 ==============================================================================
 
 STREAM ID                            S3           S4           S5           S6
        NAME
        PHASE                      VAPOR        VAPOR        MIXED        MIXED
  
 -----  TOTAL STREAM  -----
 RATE, LB-MOL/HR                3759.105     2624.452     2625.667     2625.667
       M LB/HR                    42.284       42.271       42.290       42.290
 STD LIQ RATE, FT3/HR           2216.791     1808.644     1809.481     1809.481
 TEMPERATURE, F                  300.000      435.000      227.289      120.000
 PRESSURE, PSIA                  505.000      490.000      485.000      480.000
 MOLECULAR WEIGHT                 11.248       16.106       16.106       16.106
 ENTHALPY, MM BTU/HR              18.310       20.218       10.706        5.370
           BTU/LB                433.033      478.298      253.166      126.972
 MOLE FRACTION LIQUID              .0000        .0000        .0910        .1519
 REDUCED TEMP (KAYS RULE)         4.2157       3.8931       2.9893       2.5224
         PRES (KAYS RULE)         1.8718       1.7055       1.6881       1.6707
 ACENTRIC FACTOR                  -.1607       -.1349       -.1349       -.1349
 WATSON K (UOPK)                  16.133       15.044       15.046       15.046
 STD LIQ DENSITY, LB/FT3          19.074       23.371       23.371       23.371
         SPECIFIC GRAVITY          .3058        .3747        .3747        .3747
         API GRAVITY             331.158      246.093      246.093      246.093
 
 --------  VAPOR  ---------
 RATE, LB-MOL/HR                3759.105     2624.452     2386.698     2226.737
       M LB/HR                    42.284       42.271       22.710        9.474
       M FT3/HR                   60.744       51.363       36.336       29.050
 STD VAP RATE(1), M FT3/HR      1426.518      995.936      905.712      845.010
 SPECIFIC GRAVITY (AIR=1.0)         .388         .556         .329         .147
 MOLECULAR WEIGHT                 11.248       16.106        9.515        4.255
 ENTHALPY, BTU/LB                433.033      478.298      390.506      420.793
 CP, BTU/LB-F                       .858         .837         .989        1.749
 DENSITY, LB/M FT3               696.096      822.980      625.005      326.121
 Z (FROM DENSITY)                 1.0010        .9988       1.0016       1.0066
 
 --------  LIQUID  --------
 RATE, LB-MOL/HR                     N/A          N/A      238.969      398.930
       M LB/HR                       N/A          N/A       19.583       32.834
       FT3/HR                        N/A          N/A      451.901      696.163
       GAL/MIN                       N/A          N/A       56.341       86.794
 STD LIQ RATE, FT3/HR                N/A          N/A      401.718      672.527
 SPECIFIC GRAVITY (H2O=1.0)          N/A          N/A        .7816        .7828
 MOLECULAR WEIGHT                    N/A          N/A       81.948       82.306
 ENTHALPY, BTU/LB                    N/A          N/A       93.852       42.124
 CP, BTU/LB-F                        N/A          N/A         .522         .438
 DENSITY, LB/FT3                     N/A          N/A       43.335       47.165
 Z (FROM DENSITY)                    N/A          N/A        .1244        .1347
 
  (1) STANDARD VAPOR VOLUME IS 379.49 FT3/LB-MOLE (60 F AND 14.696 PSIA)


 SIMULATION SCIENCES INC.          R                                  PAGE P-21
 PROJECT                     PRO/II  VERSION 5.0 ELEC V5.4               386/EM
 PROBLEM                                 OUTPUT                                
                                     STREAM SUMMARY                    10/06/98
 ==============================================================================
 
 STREAM ID                            S7           S8           S9          TOP
        NAME
        PHASE                      VAPOR        VAPOR        VAPOR        VAPOR
  
 -----  TOTAL STREAM  -----
 RATE, LB-MOL/HR                2226.737     1781.390     1581.097       36.134
       M LB/HR                     9.474        7.579        3.742        2.333
 STD LIQ RATE, FT3/HR           1137.227      909.782      745.768       49.263
 TEMPERATURE, F                  120.000      120.000       60.000      155.541
 PRESSURE, PSIA                  480.000      480.000       14.696       14.700
 MOLECULAR WEIGHT                  4.255        4.255        2.367       64.574
 ENTHALPY, MM BTU/HR               3.987        3.189        1.828         .506
           BTU/LB                420.793      420.793      488.533      217.060
 MOLE FRACTION LIQUID              .0000        .0000        .0000        .0000
 REDUCED TEMP (KAYS RULE)         6.0687       6.0687       7.7646        .7562
         PRES (KAYS RULE)         2.0621       2.0621        .0734        .0251
 ACENTRIC FACTOR                  -.1954       -.1954       -.2142        .1321
 WATSON K (UOPK)                  29.231       29.231       42.713       10.797
 STD LIQ DENSITY, LB/FT3           8.331        8.331        5.018       47.363
         SPECIFIC GRAVITY          .1336        .1336        .0805        .7594
         API GRAVITY             927.828      927.828     1627.294       54.821
 
 --------  VAPOR  ---------
 RATE, LB-MOL/HR                2226.737     1781.390     1581.097       36.134
       M LB/HR                     9.474        7.579        3.742        2.333
       M FT3/HR                   29.050       23.240      600.142       15.884
 STD VAP RATE(1), M FT3/HR       845.010      676.008      600.000       13.712
 SPECIFIC GRAVITY (AIR=1.0)         .147         .147    8.171E-02        2.229
 MOLECULAR WEIGHT                  4.255        4.255        2.367       64.574
 ENTHALPY, BTU/LB                420.793      420.793      488.533      217.060
 CP, BTU/LB-F                      1.749        1.749        2.917         .348
 DENSITY, LB/M FT3               326.121      326.121        6.235      146.894
 Z (FROM DENSITY)                 1.0066       1.0066       1.0002        .9788
 
 --------  LIQUID  --------
 RATE, LB-MOL/HR                     N/A          N/A          N/A          N/A
       M LB/HR                       N/A          N/A          N/A          N/A
       FT3/HR                        N/A          N/A          N/A          N/A
       GAL/MIN                       N/A          N/A          N/A          N/A
 STD LIQ RATE, FT3/HR                N/A          N/A          N/A          N/A
 SPECIFIC GRAVITY (H2O=1.0)          N/A          N/A          N/A          N/A
 MOLECULAR WEIGHT                    N/A          N/A          N/A          N/A
 ENTHALPY, BTU/LB                    N/A          N/A          N/A          N/A
 CP, BTU/LB-F                        N/A          N/A          N/A          N/A
 DENSITY, LB/FT3                     N/A          N/A          N/A          N/A
 Z (FROM DENSITY)                    N/A          N/A          N/A          N/A
 
  (1) STANDARD VAPOR VOLUME IS 379.49 FT3/LB-MOLE (60 F AND 14.696 PSIA)