PRO II with Provision 5.0

- Open a New file.

- Make the necessary changes in your system of units by clicking on the icon that shows a ruler.

- Set the Thermodynamic Package by clicking on the icon that shows an equilibrium line.

- Open Category: ‘Most Commonly Used’.

- Primary Method: choose the appropriate one.

- Modify: this is optional but you may need to do some modifications of the methods that are used to calculate different properties of your system (ie.: enthalpies, densities, entropies, etc.)

- Load the components of your system by clicking on the icon that shows a benzene ring.

- ‘Select from List’

- Here you have several options: it will save you some time if you do a Search String.

- Click on the component you want and then click on ‘Add Component’

- Continue adding the rest of the species of your case problem.

- Finally, click ‘OK’.

- Start setting up your equipment and their interconnecting streams. Use the PFD Palette.

- When you are done with the equipment and streams you will need to specify the conditions (i.e.: temperatures, pressures, vapor or liquid fraction, etc), compositions and any other piece of information (heat duties, system characteristics such as adiabatic, isothermal, etc.).  YOU WILL NOT BE ABLE TO RUN YOUR SIMULATION UNTIL ALL THE MINIMUM NECESSARY INFORMATION HAS BEEN LOADED (you may know before hand how many specifications you will need by calculating the degrees of freedom of your system).

- Click ‘Run’ in the Run Palette and start praying…

- Once you are done you may save your case by going to ‘File’ and then ‘Save As…’.

- If you are required to submit your simulation you will have to create a keyword file by going to ‘File’ and then ‘Export’. This will create a file with the name you chose and the extension *.inp.