TWO PHASE FLUID FLOW

DISPERSED

ANNULAR

STRATIFIED

FROTH

WAVY

SLUG

PLUG

BUBBLE

TWO EXTREME CASES

- Vapor and Liquid in Equilibrium (Benzene 40%, Toluene 60%)

- Liquid and gas (air and benzene)

IMPORTANT:

PHASES TRAVEL AT DIFFERENT VELOCITIES!!!

TYPICAL VELOCITIES

REGIME	  LIQUID VEL.	VAPOR VEL.

(ft/sec)				(ft/Sec)

Dispersed	       Close to vapor			  > 200

Annular				<0.5 			  > 20

Stratified				<0.5 			  0.5-10

Slug				15 (But less than vapor vel.)		        3-50

Plug					  2 				    < 4

Bubble				5-15 			   0.5-2

PREDICTION OF FLOW PATTERNS

BAKER PLOT

NOTE:

- ( and (  depend on the fluid property only

- BX  depends on the ratio of flows (Known beforehand. Not a design parameter)

- BY  depends on the vapor/gas superficial velocity. This is the only parameter the designer can change (through A)

- Transition boundaries are not at all that sharp.

TRAJECTORIES ON THE BAKER PLOT

(or ...... how regimes change on a pipe.)

As the pressure drop is large, then the density of the vapor is lower.

1) ( ( ~ 		BX  ~  BX  decreases

2)   ~ 		BY  ~  BY  increases

Thus trajectories are always "up" and "to the left"

PRESSURE DROP

Lockart and Martinelli (1949)

where

a                     b

Bubble                   14.2                0.75

Slug                       1190               0.82

Stratified               15400              1

(horizontal)

Plug                       27.3                0.86

Annular             4.8 -0.3125D      0.343-0.021D

DISPERSED

WAVE

Pressure Drop Due to Gravity

Pressure Drop Due to Acceleration

# Text boxes

(cp)

(ft2)

(lb/h)

(dyn/cm)

(lb/ft3)

Pressure Drop of the vapor only, without the liquid present!

Pressure Drop of the liquid only, without the vapor present!

ID (in). Pipes 12" and over use D=12

VOID FRACTION

Mass Quality =Wg/(Wg+WL)