DEPRECIATION

Reduction in value due to any causes.

Example: Pump

Cost :                       CV= $12,000

Scrap value :			VS= $2,000

Depreciation :    		     = $10,000

For engineers, depreciation is considered as a cost for using the equipment.

TYPES OF DEPRECIATION

Functional: wear and Tear, corrosion, accidents, age deterioration.

Obsolescence: Due to technological advances.

Depletion: Loss due to materials consumed. Applicable to Natural Resources (timber, mineral, oil deposits)

SERVICE LIFE

The IRS has determined various values

(See P&T for complete list).

Group 1: General Business Assets. (Office furniture, Land, Buildings, etc)

Group 2: Non-manufacturing activities: (Agriculture, Fishing, Mining, etc.)

Group 3: Manufacturing. Examples. Petroleum Refining: 16 years. Chemicals 11 years.

Group 4: Transportation, Communication and Public Utilities: (Electrical, Gas, Motor transport, Radio and TV broadcasting, railroad, etc.)

SALVAGE VALUE

Net cash obtainable from the sale of used property (above charges for removal and sale)

Scrap value: Salvage value after dismantling a unit.

PRESENT VALUE

Book Value    : Original Cost - All

Depreciation.

Market Value : Cash obtainable from

selling the unit.

Replacement Value : Cost of

obtaining the

same property.

METHODS TO CALCULATE DEPRECIATION

Straight  Line Depreciation :

Value decreases linearly in time.

d=

d:  Depreciation ($/year)

V : Original value

VS: Salvage value.

n :  Service life

Book Value :

Va=V-a d

a : number of years of use.

Multiple Straight  Line Depreciation:

Re-estimates the service life and salvage value every account period end.

Declining balance or Fixed % Method:

Depreciation (d) is a fixed % of the property value at the beginning of the year.

Let f be the fixed % factor.

End of first year :    d= V f

Va= V(1-f)

End of 2nd year :    d= V(1-f) f

Va= V(1-f)2

End of nth year :     d= V(1-f)n-1 f

Va= V(1-f)n=VS

==>		f= 1 -

(Matheson Formula)

Sum of the years method:

Depreciation factor is given by the numbers of years of service left divided by the sum of the years of service.

Depreciation factor at year ‘a’ is given by

fa =

Example:  V= $ 22,000, VS=$ 2,000.; n=10

Year			fa		da=(V-VS)fa		Va

1			10/55		 $ 3636	   $18,364

2			 9/55		 $ 3272	   $15,092

3 		 8/55		 $ 2909	   $12,183

:

9			 2/55		 $ 727   	   $ 2363

10		1/55            $ 363          $ 2000

V-Vs: total depreciable value

COMPARISON

Declining Balance vs. Straight Line:

Advantage :  Higher on early days.

Disadvantage : Puts too much emphasis on Salvage value. Does not even work for VS=0.

See figure 9-2 P&T page 281

Sinking fund method:

Depreciation allowance is considered as a payment of an annuity used to recover the capital at the end of the period.

Payments:

R= (V-VS)

Total Depreciation after a years  =  V-Va

Amount accumulated  =  R

Va= V-(V-VS)

Double Declining Method

Tax laws accept rates of depreciation up to two times the straight-line depreciation rate assuming zero scrap value.

==>  				f =

Consider n=10 Then  f=2/10

After 5 years:

Va= V(1-f)5

and           (Va/V)= (1-0.02)5 ~ 0.32

Approximately 2/3 is written of after 1/2 life

Percentage written off at half life:

n		(1-2/n)n/2

4			0.25

6			0.29

8			0.31

10			0.32

20			0.35

Combination Method

The Double declining method does not give scrap value VS at the end of service life

The Combination Method assumes

first half-life       :        Double declining

Second half-life :       Straight line