Piping Strength

Bursting pressure of a pipe

= Mean Diameter

= Wall Thickness

= Tensile Strength (properties of material and fabricate)

= Bursting pressure

Safe Working Pressure

Schedule of a Pipe (ASA)

There are 10 Sch numbers

10, 20, 30, 40, 60, 80, 100, 120, 140, 160

(You specify a pipe by giving the diameter and the Schedule

- Get pressure inside    Pin  (psia)

- PS  =  Pin - 14.696

- ; SS ==> Characteristic of pipe (6500 - 9000 psi)

- Pick lower possible Sch standard