COLUMN: SPECIFICATION AND VARIABLES

Consider a column with  		NT trays

NC components

EQUATIONS:

1) Steady state mass balances for all components in all trays

Lj-1 xj-1,i-[(Lj+LDj)xj,i+(Vj+VDj)yj,i]+Vj+1yj+1,i+Fjzi=0       	i=1,..,NC    j=1,..., NT

L= Liquid rates 				V= Vapor rates

LD= Liquid Draw rates 			VD= Vapor Draw rates

x= liquid compositions			y=vapor compositions

z= feed composition

2) Equilibrium Relations

yj,i=Kj,i,(xj, Tj, Pj)xj,i 						i=1,..,NC    j=1,..., NT

3) Summation equations

xj,i= 1			j=1,..., NT

yj,i= 1			j=1,..., NT

3) Enthalpy balance in each tray

Lj-1 hj-1-[(Lj+LDj)hj+(Vj+VDj)Hj]+Vj+1Hj+1+FjHF=0        	 j=1,..., NT

h: liquid enthalpy					H: Vapor enthalpy

HF: Enthalpy of feed

Total number of equations: NT(3+2NC)

VARIABLES

1) For each tray (excluding condenser and reboiler):

Tj  , Lj  , Vj  , xj,i  , yj,i			        Variables= 3( NT -2) + 2 (NT-2) NC

2) For the condenser  (temperature, flows, compositions and duty)

T1  , L1 , D  , x1,i  , y1,i  , QC		        Variables= 3+ 2 NC+1

3) For the reboiler  (temperature, flows, compositions and duty)

TNc  , VNc , B  , xNc,i   ,  yNc,i , QR	        Variables= 3+ 2 NC+1

Total number of Variables: NT(3+2NC)+2

Unknowns- equations = 2

Therefore two specifications are needed : Either through fixing some values or by adding some equations.

TIPS FOR DISTILLATION COLUMN SETUP

1.	DO NOT TRY BLINDLY SPECS AND NUMBER OF TRAYS. IT WON’T WORK MOST OF THE TIME.

2.	IF YOU HAVE MANY COMPONENTS, DO NOT INCLUDE ALL OF THEM AT THE BEGINNING. START WITH A FEW ABUNDANT COMPONENTS.

3.	RUN AN ADIABATIC FLASH FIRST. IF THE FEED IS NOT TWO PHASE AT THE DESIRED PRESSURE, PUT AN ISOTHERMAL FLASH. CHANGE THE TEMPERATURE UNTIL YOU GET SOME SEPARATION IN THE DIRECTION YOU WANT.

To do this, list the components in increasing NBP and determine your key components. The light goes through the top and the heavy key component goes through the bottom

4.	REPLACE THE FLASH BY A COLUMN WITH THREE PLATES. USE BOTTOM SPEC SIMILAR (A LITTLE MORE TIGHT) TO THE GIVEN BY THE FLASH OUTLET STREAM. SPECIFY SOME REFLUX RATIO. Be careful with the use of a total condenser if you have inert or highly volatile compounds.

5.	ADD  MISSING  COMPONENTS.   INCREASE  SLOWLY THEIR CONCENTRATION.

6.	KEEP TIGHTENING THE BOTTOM SPEC AND ADJUSTING THE REFLUX RATIO AS WELL AS INCREASING THE NUMBER OF TRAYS SO YOU MEET THE SEPARATION YOU WANT WITH A REASONABLE REFLUX RATIO.