## Slide 1: The Coupled Routing and Excess STorage (CREST) distributed hydrological model Family: Development and Application 2011-2026
01/21/2026
Hydrometeorology and Remote Sensing Laboratory
University of Oklahoma
National Weather Center, Suite 4610
Website: https://hydro.ou.edu
Notes: Change the title
website

## Slide 2: Table of content
CREST model introduction
CREST model family and milestones
Education and capacity building
Summary and future direction

## Slide 3: The Coupled Routing and Excess STorage (CREST) distributed hydrological model
A Distributed Hydrologic Model designed to take advantage of the 4-D remote sensing data, can be used at global, regional, or basin scales.
  Three soil layers.
  Distributed, fully coupled runoff generation and routing model
  Simulates water and energy fluxes and storage on a regular grid
  Cell-to-cell flow routing
2 Forcings
  Precipitation, PET
17 Parameters
  Water balance, Water routing
9 Outputs
  Streamflow, soil moisture, unit streamflow, runoff, etc.

## Slide 4: CREST Family Model: Global users, publications and Citations over 2011-2021
# of publications: 100+
# of citations: 5,072

## Slide 5: CREST Model family tree by 2026

## Slide 6: The Original Concept: Satellite-driven Global Hydrological Model
Hong, Y., R. Adler, F. Hossain, S. Curtis, and G. Huffman, 2007: A first approach to global runoff simulation using satellite rainfall estimation, Water Res. Research, 43(8). {230} The first satellite-driven global runoff real-time modeling system in supporting multi-continental hydrologic prediction
Hong, Y., R.F. Adler, A. Negri, and G.J. Huffman, 2007: Flood and landslide applications of near real-time satellite rainfall estimation, Natural Hazards, 43(2), 510-521 {238}

## Slide 7: The Birth 2011
Wang, J., Hong, Y., Li, L., Gourley, J.J., Khan, S.I., Yilmaz, K.K., Adler, R.F., Policelli, F.S., Habib, S., Irwn, D., Limaye, A.S., Korme, T., Okello, L., 2011. The coupled routing and excess storage (CREST) distributed hydrological model. Hydrological Sciences Journal 56, 84–98. {299} Introduced the remote-sensing–native, coupled routing-storage distributed model that became the foundation of the CREST model family (CREST/EF5/CRES-iMAP/CREST-VEC/iCRESLIDE/iCRESTRIGRS) used worldwide.
CREST v1.0 (2011)
1) distributed rainfall-runoff generation process and cell-to-cell routing,
2) coupled routing and runoff generation mechanisms,
3) sub-grid variability of soil moisture capacity
Funding acknowledgment of NASA USAID and NOAA

## Slide 8: Widely used version CREST v2.0, 2013-2017
(1) model implementation with options of either spatially uniform, semi-distributed, or distributed parameter values,
(2) including impervious area ratio parameter to emulate fast runoff generation,
(3) including a rainfall multiplier parameter to mitigate the impact of
rainfall bias on hydrologic predictions,
(4) automatic calibration using the SCE-UA algorithm
(5) parallel computing
(6)modular design framework and enhancement of the computation adpability using FORTRAN matrix operation to make the model more efficient
Xue, X., Hong, Y., Limaye, A.S., Gourley, J.J., Huffman, G.J., Khan, S.I., Dorji, C., Chen, S., 2013. Statistical and hydrological evaluation of TRMM-based Multi-satellite Precipitation Analysis over the Wangchu Basin of Bhutan: Are the latest satellite precipitation products 3B42V7 ready for use in ungauged basins? Journal of Hydrology 499, 91–99. https://doi.org/10.1016/j.jhydrol.2013.06.042

## Slide 9: Coupled Flood and Landslide Hazard modeling: iCRESLIDE = CREST + SLIDE, 2016
iCRESLIDE: USA National Flash Landslide System
NMQ： National Mosaic and Multi-Sensor QPE (NMQ)
FLASH： Flooded Locations And Simulated Hydrographs
LANDSLIDE: SLope-Infiltration-Distributed Equilibrium Model
NMQ Radar Precipitation Observations 250 m/2.5 min
FLASH Distributed CREST Hydrologic Models
10-11 June 2010, Albert Pike Rec Area, Arkansas
250 mm
200
150
Simulated surface water flow
20 fatalities
LANDSLIDE
Landslide Hotspot Models
Red: Observations
Pink: Predictions
Landslide prediction
Coupled the CREST model with the SLIDE model, which computes slope stability as a factor of safety.
The relatively more accurate subsurface hydrologic variables from CREST were fed to the SLIDE model in an integrated way.
He, X., Hong, Y., Vergara, H., Zhang, K., Kirstetter, P.-E., Gourley, J.J., Zhang, Y., Qiao, G., Liu, C., 2016. Development of a coupled hydrological-geotechnical framework for rainfall-induced landslides prediction. Journal of Hydrology 543, 395–405. https://doi.org/10.1016/j.jhydrol.2016.10.016
Zhang, K., Xue, X., Hong, Y., Gourley, J.J., Lu, N., Wan, Z., Hong, Z., Wooten, R., 2016. iCRESTRIGRS: a coupled modeling system for cascading flood–landslide disaster forecasting. Hydrol. Earth Syst. Sci. 20, 5035–5048. https://doi.org/10.5194/hess-20-5035-2016

## Slide 10: NOAA/NSSL Operational Flash Flood model EF5, 2017-
Ensemble framework for flash flood forecasting (EF5)
Incorporate multiple models for water balance and runoff routing to provide ensemble results
Operate in real-time to serve NWS for facilitating flood warning in the USA.
Vergara, H., Kirstetter, P.-E., Gourley, J.J., Flamig, Z.L., Hong, Y., Arthur, A., Kolar, R., 2016. Estimating a-priori kinematic wave model parameters based on regionalization for flash flood forecasting in the Conterminous United States. Journal of Hydrology 541, 421–433. https://doi.org/10.1016/j.jhydrol.2016.06.011
Clark, R.A., Flamig, Z.L., Vergara, H., Hong, Y., Gourley, J.J., Mandl, D.J., Frye, S., Handy, M., Patterson, M., 2017. Hydrological Modeling and Capacity Building in the Republic of Namibia. Bulletin of the American Meteorological Society 98, 1697–1715. https://doi.org/10.1175/BAMS-D-15-00130.1
Gourley, J.J., Flamig, Z.L., Vergara, H., Kirstetter, P.-E., Clark, R.A., Argyle, E., Arthur, A., Martinaitis, S., Terti, G., Erlingis, J.M., Hong, Y., Howard, K.W., 2017. The FLASH Project: Improving the Tools for Flash Flood Monitoring and Prediction across the United States. Bulletin of the American Meteorological Society 98, 361–372. https://doi.org/10.1175/BAMS-D-15-00247.1
Flamig, Z.L., Vergara, H., Gourley, J.J., 2020. The Ensemble Framework For Flash Flood Forecasting (EF5) v1.2: Description and Case Study (preprint). Hydrology. https://doi.org/10.5194/gmd-2020-46
Operational web viewer: https://mrms.nssl.noaa.gov/qvs/product_viewer/

## Slide 11: 2D flood inundation modeling CREST-iMAP, 2021-
CREST – inundation MApping and Prediction
Coupled the CREST v2.1 with 2D Hydraulic Model using finite volume method to solve shallow water equation.
The model produce comprehensive outputs for a flooding event: streamflow (1D), flood extent (2D), flood dept (2D), surface water speed and direction (2D), etc.
Chen, M., Li, Z., Gao, S., Luo, X., Wing, O.E.J., Shen, X., Gourley, J.J., Kolar, R.L., Hong, Y., 2021. A comprehensive flood inundation mapping for Hurricane Harvey using an integrated hydrological and hydraulic model. Journal of Hydrometeorology. https://doi.org/10.1175/JHM-D-20-0218.1
Li, Z., Chen, M., Gao, S., Luo, X., Gourley, J.J., Kirstetter, P., Yang, T., Kolar, R., McGovern, A., Wen, Y., Rao, B., Yami, T., Hong, Y., 2021. CREST-iMAP v1.0: A fully coupled hydrologic-hydraulic modeling framework dedicated to flood inundation mapping and prediction. Environmental Modelling & Software 141, 105051. https://doi.org/10.1016/j.envsoft.2021.105051
Chen, M., Li, Z., Gao, S., Xue, M., Gourley, J.J., Kolar, R.L., Hong, Y., 2022. A flood predictability study for Hurricane Harvey with the CREST-iMAP model using high-resolution quantitative precipitation forecasts and U-Net deep learning precipitation nowcasts. Journal of Hydrology 612, 128168. https://doi.org/10.1016/j.jhydrol.2022.128168
Li, Z., Chen, M., Gao, S., Wen, Y., Gourley, J.J., Yang, T., Kolar, R., Hong, Y., 2022. Can re-infiltration process be ignored for flood inundation mapping and prediction during extreme storms? A case study in Texas Gulf Coast region. Environmental Modelling & Software 155, 105450. https://doi.org/10.1016/j.envsoft.2022.105450

## Slide 12: Vector-based model and large-scale CREST-VEC simulation 2022-
CREST model with a vector-based routing scheme: CREST-VEC
Coupled the CREST v2.1 with MizuRoute water routing model
Include a vector-based lake module, surface and subsurface runoff routings
Highly computational efficient and suitable for large-scale simulations (CONUS, Li et al.,2023)
Li, Z., Gao, S., Chen, M., Gourley, J., Mizukami, N., Hong, Y., 2022. CREST-VEC: a framework towards more accurate and realistic flood simulation across scales. Geosci. Model Dev. 15, 6181–6196. https://doi.org/10.5194/gmd-15-6181-2022
Li, Z., Gao, S., Chen, M., Gourley, J.J., Hong, Y., 2022. Spatiotemporal Characteristics of US Floods: Current Status and Forecast Under a Future Warmer Climate. Earth’s Future 10, e2022EF002700. https://doi.org/10.1029/2022EF002700
Li, Z., Gao, S., Chen, M., Gourley, J.J., Liu, C., Prein, A.F., Hong, Y., 2022. The conterminous United States are projected to become more prone to flash floods in a high-end emissions scenario. Commun Earth Environ 3, 86. https://doi.org/10.1038/s43247-022-00409-6

## Slide 13: Recent developments, 2023, 2025
CREST V3.0 added a groundwater module
CREST V4.3 added a lake module and elevation-based temperature resampling
Chen, M., Li, Z., Vergara, H.J., Gourley, J.J., Xue, M., Hong, Y., Hu, X.-M., Mayol Novoa, H., Martin, E.R., McPherson, R.A., Gao, S., Vitaliano Perez, A., Yanqui Morales, I., 2023. Conus-wide model calibration and validation for CRESTv3.0 – An improved Coupled Routing and Excess STorage distributed hydrological model. Journal of Hydrology 626, 130333. https://doi.org/10.1016/j.jhydrol.2023.130333

## Slide 14: CREST-AI: AI agent for hydrological model, 2025
Leverage the advances of the LLMs, to automate the CREST model operations.
Users can interact with multi-version CREST model using plain languages.
AI calibration: has higher efficiency for users to achieve accurate CREST simulation, in-situ data is required.
Yan, S., Li, Z., Zhu, S., Wen, Y., Zhang, M., Chen, M., Cao, J., Hong, Y., 2025. AQUAH: Automatic Quantification and Unified Agent in Hydrology. https://doi.org/10.48550/ARXIV.2508.02936
Songkun Yan, Mengye Chen, Li, Z., Yixin Wen, Siyu Zhu, Mofan Zhang, et al. (2026). AI Agent for Hydrologic Modeling: Definition, Development and Application. https://doi.org/10.13140/RG.2.2.34824.48643
Notes: CREST-AI change the title.
Add the preprint.

## Slide 15: Education and capacity buildings
We transfer the technology and knowledge to build local capacity through workshops and training in Norman, Oklahoma, and anywhere in the world. Over the past 15 years, 30+ workshops have been held, with 1,000+ trainees participating in the training.
Africa: Kenya, Uganda
Asia: Pakistan, Nepal, China
Central and South America: Panama,
Colombia, Peru
CREST model was adapted by the Eastern African
Hydrological service serving Ethiopia, Uganda, Kenya,
Somalia, Rwanda, Tanzania, and Burundi

## Slide 16: Summary and future development
Since 2011, the CREST model has been successfully applied in research, hazard warning, and emergency response sectors.
The CREST model is efficient, powerful, and can produce comprehensive results for hydrological simulation and flood detection.
Years of development of the CREST model family enable various applications and solve real-world hydrological problems.
Future development
  AI integration
    CREST-AI: ML-powered hydrological model
    CREST AI agent: LLM-supported hydrological model
  Water resource management
    For arid regions
  Global flood detection
    International collaboration
  Future flood project
    WRF + CREST coupling
Notes: Delete light-weight

## Slide 17: Key Publications
Xue X., Y. Hong, A. S. Limaye, et al. (2013), Statistical and hydrological evaluation of TRMM-based Multi-satellite Precipitation Analysis over the Wangchu Basin of Bhutan: Are the latest satellite precipitation products 3B42V7 ready for use in ungauged basins? Journal of Hydrology, 499(0): 91-99. doi: 10.1016/j.jhydrol.2013.06.042. (Introduction of CREST v2.0)
Wang. J., Y. Hong, L. Li, J.J. Gourley, K. Yilmaz, S. I. Khan, F.S. Policelli, R.F. Adler, S. Habib, D. Irwn, S.A. Limaye, T. Korme, and L. Okello, 2011: The Coupled Routing and Excess STorage (CREST) distributed hydrological model. Hydrol. Sciences Journal, 56, 84-98. (Detailed Description of CREST v1.x)
Zhang, Y., Y. Hong, et al., 2014: Hydrometeorological Analysis and Remote Sensing of Extremes: Was the July 2012 Beijing Flood Event Detectable and Predictable by Global Satellite Observing and Global Weather Modeling Systems?, Journal of Hydrometeorology, doi: 10.1175/JHM-D-14-0048.1
Khan, S. I., P. Adhikari, Y. Hong, H. Vergara, T. Grout, R. F. Adler, F. Policelli, D. Irwin, T. Korme, and L. Okello, 2011: Observed and simulated hydroclimatology using distributed hydrologic model from in-situ and multi-satellite remote sensing datasets in Lake Victoria region in East Africa, Hydrol. Earth Syst. Sci. Discuss., 7, 4785-4816, doi: 10.5194/hessd-7-4785.
Khan, S. I., Y. Hong, H. J. Vergara, et al. (2012), Microwave Satellite Data for Hydrologic Modeling in Ungauged Basins, Geoscience and Remote Sensing Letters, IEEE, 9(4), 663-667
Khan, S. I., Y. Hong, J. Wang, K.K. Yilmaz, J.J. Gourley, R.F. Adler, G.R. Brakenridge, F. Policelli, S. Habib, and D. Irwin, 2011: Satellite Remote Sensing and Hydrologic Modeling for Flood Inundation Mapping in Lake Victoria Basin: Implications for Hydrologic Prediction in Ungauged Basins, IEEE Transactions on Geosciences and Remote Sensing, 49(1), 85-95, Jan. 2011, doi: 10.1109/TGRS.2010.2057513.
Shen, X., Hong, Y., Zhang, K., Hao, Z., and Wang, D. (2014) “CREST v2. 1 Refined by a Distributed Linear Reservoir Routing Scheme.” Proc., AGU Fall Meeting, H33G-0918.
Chen, M., Li, Z., Gao, S., Luo, X., Wing, O.E.J., Shen, X., Gourley, J.J., Kolar, R.L., Hong, Y., 2021. A comprehensive flood inundation mapping for Hurricane Harvey using an integrated hydrological and hydraulic model. Journal of Hydrometeorology. doi: 10.1175/JHM-D-20-0218.1
Chen, M., Li, Z., Gao, S., Xue, M., Gourley, J.J., Kolar, R.L., Hong, Y., 2022. A flood predictability study for Hurricane Harvey with the CREST-iMAP model using high-resolution quantitative precipitation forecasts and U-Net deep learning precipitation nowcasts. Journal of Hydrology 612, 128168. doi: 10.1016/j.jhydrol.2022.128168
Chen, M., Li, Z., Vergara, H.J., Gourley, J.J., Xue, M., Hong, Y., Hu, X.-M., Mayol Novoa, H., Martin, E.R., McPherson, R.A., Gao, S., Vitaliano Perez, A., Yanqui Morales, I., 2023. Conus-wide model calibration and validation for CRESTv3.0 – An improved Coupled Routing and Excess STorage distributed hydrological model. Journal of Hydrology 626, 130333. doi: 10.1016/j.jhydrol.2023.130333
Xue, X., Zhang, K., Hong, Y., Gourley, J.J., Kellogg, W., McPherson, R.A., Wan, Z., Austin, B.N., 2016. New multisite cascading calibration approach for hydrological models: case study in the Red River Basin using the VIC model. Journal of Hydrologic Engineering 21. https://doi.org/10.1061/(ASCE)HE.1943-5584.0001282.
Clark, R.A., Flamig, Z.L., Vergara, H., Hong, Y., Gourley, J.J., Mandl, D.J., Frye, S., Handy, M., Patterson, M., 2017. Hydrological Modeling and Capacity Building in the Republic of Namibia. Bulletin of the American Meteorological Society 98, 1697–1715. doi: 10.1175/BAMS-D-15-00130.1
Flamig, Z.L., Vergara, H., Gourley, J.J., 2020. The Ensemble Framework For Flash Flood Forecasting (EF5) v1.2: Description and Case Study (preprint). Hydrology. doi: 10.5194/gmd-2020-46
Gourley, J.J., Flamig, Z.L., Vergara, H., Kirstetter, P.-E., Clark, R.A., Argyle, E., Arthur, A., Martinaitis, S., Terti, G., Erlingis, J.M., Hong, Y., Howard, K.W., 2017. The FLASH Project: Improving the Tools for Flash Flood Monitoring and Prediction across the United States. Bulletin of the American Meteorological Society 98, 361–372. doi: 10.1175/BAMS-D-15-00247.1
Li, Z., Chen, M., Gao, S., Luo, X., Gourley, J.J., Kirstetter, P., Yang, T., Kolar, R., McGovern, A., Wen, Y., Rao, B., Yami, T., Hong, Y., 2021. CREST-iMAP v1.0: A fully coupled hydrologic-hydraulic modeling framework dedicated to flood inundation mapping and prediction. Environmental Modelling & Software 141, 105051. doi: 10.1016/j.envsoft.2021.105051
Li, Z., Gao, S., Chen, M., Gourley, J., Mizukami, N., Hong, Y., 2022a. CREST-VEC: a framework towards more accurate and realistic flood simulation across scales. Geosci. Model Dev. 15, 6181–6196. doi: 10.5194/gmd-15-6181-2022
Li, Z., Gao, S., Chen, M., Gourley, J.J., Hong, Y., 2022b. Spatiotemporal Characteristics of US Floods: Current Status and Forecast Under a Future Warmer Climate. Earth’s Future 10, e2022EF002700. doi: 10.1029/2022EF002700
Li, Z., Gao, S., Chen, M., Gourley, J.J., Liu, C., Prein, A.F., Hong, Y., 2022c. The conterminous United States are projected to become more prone to flash floods in a high-end emissions scenario. Commun Earth Environ 3, 86. https://doi.org/10.1038/s43247-022-00409-6
Li, Z., Chen, M., Gao, S., Wen, Y., Gourley, J. J., Yang, T., Kolar, R., Hong, Y., 2022. Can re-infiltration process be ignored for flood inundation mapping and prediction during extreme storms? A case study in Texas Gulf Coast region. Environmental Modelling & Software, 155, 105450.
Shen, X., Hong, Y., Zhang, K., Hao, Z., 2017. Refining a Distributed Linear Reservoir Routing Method to Improve Performance of the CREST Model. J. Hydrol. Eng. 22, 04016061. https://doi.org/10.1061/(ASCE)HE.1943-5584.0001442 (Description of CREST v2.1)
Vergara, H., Kirstetter, P.-E., Gourley, J.J., Flamig, Z.L., Hong, Y., Arthur, A., Kolar, R., 2016. Estimating a-priori kinematic wave model parameters based on regionalization for flash flood forecasting in the Conterminous United States. Journal of Hydrology 541, 421–433. https://doi.org/10.1016/j.jhydrol.2016.06.011
Wang, J., Hong, Y., Li, L., Gourley, J.J., Khan, S.I., Yilmaz, K.K., Adler, R.F., Policelli, F.S., Habib, S., Irwn, D., Limaye, A.S., Korme, T., Okello, L., 2011. The coupled routing and excess storage (CREST) distributed hydrological model. Hydrological Sciences Journal 56, 84–98. https://doi.org/10.1080/02626667.2010.543087
Yan, S., Li, Z., Zhu, S., Wen, Y., Zhang, M., Chen, M., Cao, J., Hong, Y., 2025. AQUAH: Automatic Quantification and Unified Agent in Hydrology. https://doi.org/10.48550/ARXIV.2508.02936

## Slide 18: Thank you!
Any inquiry or questions, please email:
hydros@ou.edu
Address: HyDROS Lab
National Weather Center
120 David L. Boren Blvd., Suite 4610
Norman, OK 73072