## Slide 1
What does it mean to be “digital?”

## Slide 2
Bockus Payne Architects, Zarrow Hall, Norman, OK, 2011
image: Kirkpatrick Forest Curtis Engineering

## Slide 3
image: Andrea Pistolesi/Getty Images
Zaha Hadid Architects, Heydar Aliyev Centre, Baku, Azerbaijan, 2012

## Slide 4
Automation of manual processes
Computer as a tool to draw or visualize (CAD, vector graphics, etc.)
LEAST DIGITAL MOST DIGITAL
Using computer to do non-digital work.
Mimicking traditional workflow.
?

## Slide 5
I’ll go “draw” that up…
I’m going to go write an algorithm and cull the output domain for instantiations that satisfy my aesthetic and performance criteria.
vs.

## Slide 6
I’ll go “draw” that up…
I’m going to go write an algorithm and cull the output domain for instantiations that satisfy my aesthetic and performance criteria.
= computational thinking
vs.

## Slide 7
Automation of manual processes
Computer as a tool to draw or visualize (CAD, vector graphics, etc.)
LEAST DIGITAL MOST DIGITAL
Can use physical constructions to introduce digital principles
Computational and Algorithmic
Logical sequence of operations
or relationships
RULES-BASED DESIGN
Using computer to do non-digital work.
Mimicking traditional workflow.

## Slide 8
WALL DRAWING
BOSTON MUSEUM
On a wall surface, any
continuous stretch of wall,
using a hard pencil, place
fifty points at random.
The points should be evenly
distributed over the area
of the wall. All of the
points should be connected
by straight lines.
SOL LEWITT
(Wall drawing, Boston Museum
Pencil)

## Slide 9
Computational Drawings

## Slide 10
Rationalization
(or, the current schism in architecture)

## Slide 18
research question:
What are possible methods of designing and fabricating a structure built from plywood that eliminate frame elements, and rely on the strength of the sheet material itself?

## Slide 19
Synclastic
Anticlastic
Flat
(ruled)
Cylindrical
(ruled)
Hyperbolic Paraboloid
(ruled)
Developable ribbon
(ruled)

## Slide 20
Solution (written in pseudo-code):
1. Construct a 3D geometry that balances:
Maximum surface curvature
Maximum internal volume
2. Convert to a high resolution mesh surface
3. Reduce mesh count (create irregular polygon)
4. Measure to make sure overall size is within allowable dimensions
If not, repeat step 3, mesh reduction
5. Arrange flat patterns onto 5’x5’ sheets
If they do not fit efficiently, repeat step 3, mesh reduction
6. Distribute joints along edges
7. Perform Boolean operation at joints
8. Import panels with joints into CAM (Computer Automated Manufacturing) application
9. Create toolpaths
10. CNC mill from plywood panels
11. Assemble

## Slide 29
G90
M3
(Fingers 1)
T1
S24000
M3
G0 Z2.0000
G0 X4.3182 Y4.9925
G1 X4.3182 Y4.9925 Z0.5240 F80.
G1 X4.3182 Y4.9925 Z0.4990 F100.
G1 X5.2354 Y4.9925 Z0.0010 F50.
G1 X5.2362 Y4.9925 Z0.0010
G1 X5.2362 Y5.0225 Z0.0010 F100.
G1 X5.2354 Y5.0225 Z0.0010
G1 X4.3186 Y5.0225 Z0.4990
G1 X4.3186 Y5.0225 Z0.5240 F250.
G0 Z0.5240
G0 X4.3191 Y5.0525
G1 X4.3191 Y5.0525 Z0.4990 F100.
G1 X5.2354 Y5.0525 Z0.0010
G1 X5.2362 Y5.0525 Z0.0010
G1 X5.2362 Y5.0825 Z0.0010
G1 X5.2354 Y5.0825 Z0.0010
G1 X4.9237 Y5.0825 Z0.1711
G1 X4.3198 Y5.0825 Z0.4990
G1 X4.3198 Y5.0825 Z0.5240 F250.
G0 Z0.5240
G0 X4.3211 Y5.1125
G1 X4.3211 Y5.1125 Z0.4990 F100.
G1 X4.7567 Y5.1125 Z0.2624
G1 X4.8817 Y5.1125 Z0.1943
G1 X5.0067 Y5.1125 Z0.1265
G1 X5.0692 Y5.1125 Z0.0924
G1 X5.2354 Y5.1125 Z0.0010
G1 X5.2362 Y5.1125 Z0.0010
G1 X5.2362 Y5.1425 Z0.0010
G1 X5.2354 Y5.1425 Z0.0010
G1 X5.0800 Y5.1425 Z0.0872
G1 X4.9784 Y5.1425 Z0.1423
G1 X4.8456 Y5.1425 Z0.2152
G1 X4.3225 Y5.1425 Z0.4990
G1 X4.3225 Y5.1425 Z0.5240 F250.
G0 Z0.5240
G0 X4.3246 Y5.1725
G1 X4.3246 Y5.1725 Z0.4990 F100.
G1 X4.6974 Y5.1725 Z0.2968
G1 X4.7755 Y5.1725 Z0.2540
G1 X4.9161 Y5.1725 Z0.1780
G1 X4.9786 Y5.1725 Z0.1436
G1 X5.0333 Y5.1725 Z0.1132
G1 X5.0724 Y5.1725 Z0.0921
G1 X5.1271 Y5.1725 Z0.0619
G1 X5.2355 Y5.1725 Z0.0010
G1 X5.2362 Y5.1725 Z0.0010
G1 X4.8769 Y5.2625 Z0.2044
G1 X4.7987 Y5.2625 Z0.2464
G1 X4.7675 Y5.2625 Z0.2639
G1 X4.7128 Y5.2625 Z0.2938
G1 X4.5487 Y5.2625 Z0.3822
G1 X4.4862 Y5.2625 Z0.4163
G1 X4.3334 Y5.2625 Z0.4990
G0 Z0.4990
G0 X4.3370 Y5.2925
G1 X4.6155 Y5.2925 Z0.3488 F100.
G1 X4.6780 Y5.2925 Z0.3145
G1 X4.7717 Y5.2925 Z0.2642
G1 X4.8342 Y5.2925 Z0.2298
G1 X4.8576 Y5.2925 Z0.2165
G1 X4.8967 Y5.2925 Z0.1957
G1 X4.9592 Y5.2925 Z0.1611
G1 X4.9905 Y5.2925 Z0.1432
G1 X5.0217 Y5.2925 Z0.1262
G1 X5.0530 Y5.2925 Z0.1087
G1 X5.0998 Y5.2925 Z0.0813
G1 X5.1155 Y5.2925 Z0.0725
G1 X5.1467 Y5.2925 Z0.0545
G1 X5.1780 Y5.2925 Z0.0358
G1 X5.2356 Y5.2925 Z0.0010
G1 X5.2362 Y5.2925 Z0.0010
G1 X5.2362 Y5.3225 Z0.0010
G1 X5.2356 Y5.3225 Z0.0010
G1 X5.1737 Y5.3225 Z0.0393
G1 X5.1425 Y5.3225 Z0.0582
G1 X5.1073 Y5.3225 Z0.0785
G1 X5.0800 Y5.3225 Z0.0950
G1 X5.0487 Y5.3225 Z0.1131
G1 X5.0058 Y5.3225 Z0.1369
G1 X4.9862 Y5.3225 Z0.1483
G1 X4.9550 Y5.3225 Z0.1661
G1 X4.9237 Y5.3225 Z0.1833
G1 X4.8905 Y5.3225 Z0.2011
G1 X4.8612 Y5.3225 Z0.2178
G1 X4.8300 Y5.3225 Z0.2352
G1 X4.7987 Y5.3225 Z0.2520
G1 X4.7440 Y5.3225 Z0.2812
G1 X4.6659 Y5.3225 Z0.3242
G1 X4.5331 Y5.3225 Z0.3955
G1 X4.4862 Y5.3225 Z0.4211
G1 X4.3416 Y5.3225 Z0.4990
G1 X4.3416 Y5.3225 Z0.5240 F250.
G0 Z0.5240
G0 X4.3464 Y5.3525
G1 X4.3464 Y5.3525 Z0.4990 F100.
G1 X4.5930 Y5.3525 Z0.3665
G1 X4.6321 Y5.3525 Z0.3450
G1 X4.7180 Y5.3525 Z0.2991
G1 X4.7805 Y5.3525 Z0.2647
G1 X4.7962 Y5.3525 Z0.2559
G1 X5.1868 Y5.3525 Z0.0321
G1 X5.1184 Y5.3525 Z0.0737
G1 X5.1555 Y5.3525 Z0.0517
G1 X5.1868 Y5.3525 Z0.0321
G1 X5.2357 Y5.3525 Z0.0010
G1 X5.2362 Y5.3525 Z0.0010
G1 X5.2362 Y5.3825 Z0.0010
G1 X5.2357 Y5.3825 Z0.0010
G1 X5.1737 Y5.3825 Z0.0416
G1 X5.1425 Y5.3825 Z0.0611
G1 X5.1190 Y5.3825 Z0.0752
G1 X5.1112 Y5.3825 Z0.0802
G1 X5.0800 Y5.3825 Z0.0994
G1 X5.0487 Y5.3825 Z0.1177
G1 X5.0312 Y5.3825 Z0.1276
G1 X5.0175 Y5.3825 Z0.1359
G1 X4.9862 Y5.3825 Z0.1542
G1 X4.9550 Y5.3825 Z0.1718
G1 X4.9355 Y5.3825 Z0.1824
G1 X4.9237 Y5.3825 Z0.1892
G1 X4.8925 Y5.3825 Z0.2071
G1 X4.8612 Y5.3825 Z0.2243
G1 X4.8261 Y5.3825 Z0.2430
G1 X4.7987 Y5.3825 Z0.2586
G1 X4.7675 Y5.3825 Z0.2758
G1 X4.6933 Y5.3825 Z0.3153
G1 X4.6737 Y5.3825 Z0.3263
G1 X4.6425 Y5.3825 Z0.3434
G1 X4.5097 Y5.3825 Z0.4144
G1 X4.4706 Y5.3825 Z0.4356
G1 X4.3524 Y5.3825 Z0.4990
G1 X4.3524 Y5.3825 Z0.5240 F250.
G0 Z0.5240
G0 X4.3587 Y5.4125
G1 X4.3587 Y5.4125 Z0.4990 F100.
G1 X4.5417 Y5.4125 Z0.4013
G1 X4.5964 Y5.4125 Z0.3715
G1 X4.6667 Y5.4125 Z0.3343
G1 X4.6979 Y5.4125 Z0.3174
G1 X4.7409 Y5.4125 Z0.2935
G1 X4.7760 Y5.4125 Z0.2750
G1 X4.7917 Y5.4125 Z0.2666
G1 X4.8229 Y5.4125 Z0.2493
G1 X4.8542 Y5.4125 Z0.2315
G1 X4.8854 Y5.4125 Z0.2147
G1 X4.9167 Y5.4125 Z0.1973
G1 X4.9518 Y5.4125 Z0.1767
G1 X4.9792 Y5.4125 Z0.1616
G1 X5.0104 Y5.4125 Z0.1434
G1 X5.0417 Y5.4125 Z0.1244
G1 X5.0729 Y5.4125 Z0.1062
G1 X5.1042 Y5.4125 Z0.0870
G1 X5.1276 Y5.4125 Z0.0719
G1 X5.1354 Y5.4125 Z0.0672
G1 X5.1667 Y5.4125 Z0.0475
G1 X5.1901 Y5.4125 Z0.0319