## Slide 1: Supercomputing in Plain English The Tyranny of the Storage Hierarchy
Henry Neeman, Director
OU Supercomputing Center for Education & Research (OSCER)
University of Oklahoma
Tuesday January 29 2013

## Slide 2: This is an experiment!
It’s the nature of these kinds of videoconferences that FAILURES ARE GUARANTEED TO HAPPEN! NO PROMISES!
So, please bear with us. Hopefully everything will work out well enough.
If you lose your connection, you can retry the same kind of connection, or try connecting another way.
Remember, if all else fails, you always have the toll free phone bridge to fall back on.

## Slide 3: H.323 (Polycom etc) #1
If you want to use H.323 videoconferencing – for example, Polycom – then:
If you AREN’T registered with the OneNet gatekeeper (which is probably the case), then:
  Dial 164.58.250.47
  Bring up the virtual keypad. On some H.323 devices, you can bring up the virtual keypad by typing: # (You may want to try without first, then with; some devices won't work with the #, but give cryptic error messages about it.)
  When asked for the conference ID, or if there's no response, enter: 0409
  On most but not all H.323 devices, you indicate the end of the ID with: #

## Slide 4: H.323 (Polycom etc) #2
If you want to use H.323 videoconferencing – for example, Polycom – then:
If you ARE already registered with the OneNet gatekeeper (most institutions aren’t), dial:
2500409
Many thanks to Skyler Donahue and Steven Haldeman of OneNet for providing this.

## Slide 5: Wowza #1
You can watch from a Windows, MacOS or Linux laptop using Wowza from either of the following URLs:
http://www.onenet.net/technical-resources/video/sipe-stream/
OR
https://vcenter.njvid.net/videos/livestreams/page1/
Wowza behaves a lot like YouTube, except live.
Many thanks to Skyler Donahue and Steven Haldeman of OneNet and Bob Gerdes of Rutgers U for providing this.

## Slide 6: Wowza #2
Wowza has been tested on multiple browsers on each of:
Windows (7 and 8): IE, Firefox, Chrome, Opera, Safari
MacOS X: Safari, Firefox
Linux: Firefox, Opera
We’ve also successfully tested it on devices with:
Android
iOS
However, we make no representations on the likelihood of it working on your device, because we don’t know which versions of Android or iOS it might or might not work with.

## Slide 7: Wowza #3
If one of the Wowza URLs fails, try switching over to the other one.
If we lose our network connection between OU and OneNet, then there may be a slight delay while we set up a direct connection to Rutgers.

## Slide 8: Toll Free Phone Bridge
IF ALL ELSE FAILS, you can use our toll free phone bridge:
800-832-0736
* 623 2847 #
Please mute yourself and use the phone to listen.
Don’t worry, we’ll call out slide numbers as we go.
Please use the phone bridge ONLY if you cannot connect any other way: the phone bridge can handle only 100 simultaneous connections, and we have over 350 participants.
Many thanks to OU CIO Loretta Early for providing the toll free phone bridge.

## Slide 9: Please Mute Yourself
No matter how you connect, please mute yourself, so that we cannot hear you.
(For Wowza, you don’t need to do that, because the information only goes from us to you, not from you to us.)
At OU, we will turn off the sound on all conferencing technologies.
That way, we won’t have problems with echo cancellation.
Of course, that means we cannot hear questions.
So for questions, you’ll need to send e-mail.

## Slide 10: Questions via E-mail Only
Ask questions by sending e-mail to:
sipe2013@gmail.com
All questions will be read out loud and then answered out loud.

## Slide 11: TENTATIVE Schedule
Tue Jan 29: Storage Hierarchy: What the Heck is Supercomputing?
Tue Jan 29: The Tyranny of the Storage Hierarchy
Tue Feb 5: Instruction Level Parallelism
Tue Feb 12: Stupid Compiler Tricks
Tue Feb 19: Shared Memory Multithreading
Tue Feb 26: Distributed Multiprocessing
Tue March 5: Applications and Types of Parallelism
Tue March 12: Multicore Madness
Tue March 19: NO SESSION (OU's Spring Break)
Tue March 26: High Throughput Computing
Tue Apr 2: GPGPU: Number Crunching in Your Graphics Card
Tue Apr 9: Grab Bag: Scientific Libraries, I/O Libraries, Visualization

## Slide 12: Supercomputing Exercises #1
Want to do the “Supercomputing in Plain English” exercises?
The second exercise will be posted soon at:
http://www.oscer.ou.edu/education/
If you don’t yet have a supercomputer account, you can get a temporary account, just for the “Supercomputing in Plain English” exercises, by sending e-mail to:
hneeman@ou.edu
Please note that this account is for doing the exercises only, and will be shut down at the end of the series. It’s also available only to those at institutions in the USA.
This week’s Introductory exercise will teach you how to compile and run jobs on OU’s big Linux cluster supercomputer, which is named Boomer.

## Slide 13: Supercomputing Exercises #2
You’ll be doing the exercises on your own (or you can work with others at your local institution if you like).
These aren’t graded, but we’re available for questions:
hneeman@ou.edu

## Slide 14: Thanks for helping!
OU IT
  OSCER operations staff (Brandon George, Dave Akin, Brett Zimmerman, Josh Alexander, Patrick Calhoun)
  Horst Severini, OSCER Associate Director for Remote & Heterogeneous Computing
  Debi Gentis, OU Research IT coordinator
  Kevin Blake, OU IT (videographer)
  Chris Kobza, OU IT (learning technologies)
  Mark McAvoy
Kyle Keys, OU National Weather Center
James Deaton, Skyler Donahue and Steven Haldeman, OneNet
Bob Gerdes, Rutgers U
Lisa Ison, U Kentucky
Paul Dave, U Chicago

## Slide 15: This is an experiment!
It’s the nature of these kinds of videoconferences that FAILURES ARE GUARANTEED TO HAPPEN! NO PROMISES!
So, please bear with us. Hopefully everything will work out well enough.
If you lose your connection, you can retry the same kind of connection, or try connecting another way.
Remember, if all else fails, you always have the toll free phone bridge to fall back on.

## Slide 16: Coming in 2013!
From Computational Biophysics to Systems Biology, May 19-21, Norman OK
Great Plains Network Annual Meeting, May 29-31, Kansas City
XSEDE2013, July 22-25, San Diego CA
IEEE Cluster 2013, Sep 23-27, Indianapolis IN
OKLAHOMA SUPERCOMPUTING SYMPOSIUM 2013, Oct 1-2, Norman OK
SC13, Nov 17-22, Denver CO

## Slide 17: OK Supercomputing Symposium 2013
2006 Keynote:
Dan Atkins
Head of NSF’s
Office of
Cyberinfrastructure
2004 Keynote:
Sangtae Kim
NSF Shared
Cyberinfrastructure
Division Director
2003 Keynote:
Peter Freeman
NSF
Computer & Information
Science & Engineering
Assistant Director
2005 Keynote:
Walt Brooks
NASA Advanced
Supercomputing
Division Director
2007 Keynote:
Jay Boisseau
Director
Texas Advanced
Computing Center
U. Texas Austin
2008 Keynote: José Munoz Deputy Office Director/ Senior Scientific Advisor NSF Office of Cyberinfrastructure
2009 Keynote: Douglass Post Chief Scientist US Dept of Defense HPC Modernization Program
FREE! Wed Oct 2 2013 @ OU
Over 235 registra2ons already!
Over 150 in the first day, over 200 in the first week, over 225 in the first month.
http://symposium2013.oscer.ou.edu/
Reception/Poster Session
Tue Oct 1 2013 @ OU
Symposium Wed Oct 2 2013 @ OU
2010 Keynote: Horst Simon Deputy Director Lawrence Berkeley National Laboratory
2013 Keynote to be announced!
2011 Keynote: Barry Schneider Program Manager National Science Foundation
2012 Keynote: Thom Dunning Director National Center for Supercomputing Applications

## Slide 18: Outline
What is the storage hierarchy?
Registers
Cache
Main Memory (RAM)
The Relationship Between RAM and Cache
The Importance of Being Local
Hard Disk
Virtual Memory
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 19: The Storage Hierarchy
Registers
Cache memory
Main memory (RAM)
Hard disk
Removable media (CD, DVD etc)
Internet
Fast, expensive, few
Slow, cheap, a lot
[5]

## Slide 20: A Laptop
Intel Core2 Duo SU9600 1.6 GHz w/3 MB L2 Cache
4 GB 1066 MHz DDR3 SDRAM
256 GB SSD Hard Drive
DVD+RW/CD-RW Drive (8x)
1 Gbps Ethernet Adapter
Dell Latitude Z600[4]

## Slide 21: Storage Speed, Size, Cost
Henry’s Laptop | Registers (Intel Core2 Duo 1.6 GHz) | Cache Memory (L2) | Main Memory (1333MHz DDR3 SDRAM) | Hard Drive | Ethernet (1000 Mbps) | DVD+R (16x) | Phone Modem (56 Kbps)
Speed (MB/sec) [peak] | 314,573[6] (12,800 MFLOP/s*) | 30,720 | 17,400 [7] | 25[9] | 125 | 22 [10] | 0.007
Size (MB) | 464 bytes** [11] | 3 | 4096 | 500,000 | unlimited | unlimited | unlimited
Cost ($/MB) | – | $32 [12] | $0.004 [12] | $0.00005 [12] | charged per month (typically) | $0.0002 [12] | charged per month (typically)
* MFLOP/s: millions of floating point operations per second
** 16 64-bit general purpose registers, 8 80-bit floating point registers,
16 128-bit floating point vector registers

## Slide 22: Registers
[25]

## Slide 23: What Are Registers?
Registers are memory-like locations inside the Central Processing Unit that hold data that are being used right now in operations.
…
Arithmetic/Logic Unit
Control Unit
Registers
Fetch Next Instruction
Add
Sub
Mult
Div
And
Or
Not
…
Integer
Floating Point
…
Fetch Data
Store Data
Increment Instruction Ptr
Execute Instruction
…
CPU
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 24: How Registers Are Used
Every arithmetic or logical operation has one or more operands and one result.
Operands are contained in source registers.
A “black box” of circuits performs the operation.
The result goes into a destination register.
Example:
addend in R0
augend in R1
ADD
sum in R2
5
7
12
Register Ri
Register Rj
Register Rk
operand
operand
result
Operation circuitry
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 25: How Many Registers?
Typically, a CPU has less than 8 KB (8192 bytes) of registers, usually split into registers for holding integer values and registers for holding floating point (real) values, plus a few special purpose registers.
Examples:
IBM POWER7 (found in IBM p-Series supercomputers): 226 64-bit integer registers and 348 128-bit merged vector/scalar registers (7376 bytes) [28]
Intel Sandy Bridge: 16 64-bit general purpose registers, 8 64-bit floating point registers, 8 128-bit floating point vector registers (320 bytes) [29]
Intel Itanium2: 128 64-bit integer registers, 128 82-bit floating point registers (2304 bytes) [23]
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 26: Cache
[4]

## Slide 27: What is Cache?
A special kind of memory where data reside that are about to be used or have just been used.
Very fast => very expensive => very small (typically 100 to 10,000 times as expensive as RAM per byte)
Data in cache can be loaded into or stored from registers at speeds comparable to the speed of performing computations.
Data that are not in cache (but that are in Main Memory) take much longer to load or store.
Cache is near the CPU: either inside the CPU or on the motherboard that the CPU sits on.
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 28: From Cache to the CPU
Typically, data move between cache and the CPU at speeds relatively near to that of the CPU performing calculations.
CPU
Cache
30 GB/sec (~2x RAM)[7]
307 GB/sec[7]

## Slide 29: Multiple Levels of Cache
Most contemporary CPUs have more than one level of cache. For example:
Intel Sandy Bridge [29]
  Level 1 caches: 32 KB instruction, 32 KB data
  Level 2 cache: 256 KB unified (instruction+data)
  Level 3 cache: 20,480 KB, shared among all cores
IBM POWER7 [28]
  Level 1 cache: 32 KB instruction, 32 KB data per core
  Level 2 cache: 256 KB unified per core
  Level 3 cache: 4096 KB unified per core
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 30: Why Multiple Levels of Cache?
The lower the level of cache:
the faster the cache can transfer data to the CPU;
the smaller that level of cache is (faster => more expensive => smaller).
Example: IBM POWER7 latency to the CPU [28]
L1 cache: 1 cycle = 0.29 ns for 3.5 GHz
L2 cache: 8.5 cycles = 2.43 ns for 3.5 GHz (average)
L3 cache: 23.5 cycles = 5.53 ns for 3.5 GHz (local to core)
RAM: 346 cycles = 98.86 ns for 3.5 GHz (1066 MHz RAM)
Example: Intel Itanium2 latency to the CPU [19]
L1 cache: 1 cycle = 1.0 ns for 1.0 GHz
L2 cache: 5 cycles = 5.0 ns for 1.0 GHz
L3 cache: 12-15 cycles = 12 – 15 ns for 1.0 GHz
Example: Intel Sandy Bridge[29]
L1 cache: 4 cycles = 2 ns @ 2.0 GHz = 32 calculations
L2 cache: 12 cycles = 6 ns @ 2.0 GHz = 96 calculations
RAM: 26-31 cycles = 13 – 15.5 ns @ 2.0 GHz = 200-248 calculations
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 31: Cache & RAM Latencies
Better
[26]
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 32: Main Memory
[13]

## Slide 33: What is Main Memory?
Where data reside for a program that is currently running
Sometimes called RAM (Random Access Memory): you can load from or store into any main memory location at any time
Sometimes called core (from magnetic “cores” that some memories used, many years ago)
Much slower => much cheaper => much bigger
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 34: What Main Memory Looks Like
…
0
1
2
3
4
5
6
7
8
9
10
536,870,911
You can think of main memory as a big long 1D array of bytes.

## Slide 35: The Relationship Between Main Memory & Cache

## Slide 36: RAM is Slow
CPU
384 GB/sec
17 GB/sec (4.4%)
Bottleneck
The speed of data transfer
between Main Memory and the
CPU is much slower than the
speed of calculating, so the CPU
spends most of its time waiting
for data to come in or go out.

## Slide 37: Why Have Cache?
CPU
Cache is much closer to the speed
of the CPU, so the CPU doesn’t
have to wait nearly as long for
stuff that’s already in cache:
it can do more
operations per second!
17 GB/sec(1%)
30 GB/sec (8%)

## Slide 38: Cache & RAM Bandwidths
Better
[26]
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 39: Cache Use Jargon
Cache Hit: the data that the CPU needs right now are already in cache.
Cache Miss: the data that the CPU needs right now are not currently in cache.
If all of your data are small enough to fit in cache, then when you run your program, you’ll get almost all cache hits (except at the very beginning), which means that your performance could be excellent!
Sadly, this rarely happens in real life: most problems of scientific or engineering interest are bigger than just a few MB.
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 40: Cache Lines
A cache line is a small, contiguous region in cache, corresponding to a contiguous region in RAM of the same size, that is loaded all at once.
Typical size: 32 to 1024 bytes
Examples
  Intel Sandy Bridge [29]
    L1 data cache: 64 bytes per line
    L2 cache: 64 bytes per line
  POWER7 [28]
    L1 instruction cache: 128 bytes per line
    L1 data cache: 128 bytes per line
    L2 cache: 128 bytes per line
    L3 cache: 128bytes per line
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 41: How Cache Works
When you request data from a particular address in Main Memory, here’s what happens:
The hardware checks whether the data for that address is already in cache. If so, it uses it.
Otherwise, it loads from Main Memory the entire cache line that contains the address.
For example, on a 2.0 GHz Sandy Bridge, a cache miss makes the program stall (wait) at least 26 cycles (13 nanoseconds) for the next cache line to load – time that could have been spent performing up to 208 calculations! [29]
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 42: If It’s in Cache, It’s Also in RAM
If a particular memory address is currently in cache, then it’s also in Main Memory (RAM).
That is, all of a program’s data are in Main Memory, but some are also in cache.
We’ll revisit this point shortly.
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 43: Mapping Cache Lines to RAM
Main memory typically maps into cache in one of three ways:
Direct mapped (occasionally)
Fully associative (very rare these days)
Set associative (common)
DON’T
PANIC!
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 44: Direct Mapped Cache
Direct Mapped Cache is a scheme in which each location in main memory corresponds to exactly one location in cache (but not the reverse, since cache is much smaller than main memory).
Typically, if a cache address is represented by c bits, and a main memory address is represented by m bits, then the cache location associated with main memory address A is MOD(A,2c); that is, the lowest c bits of A.
Example: POWER4 L1 instruction cache
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 45: Direct Mapped Cache Illustration
Must go into
cache address
11100101
Main Memory Address
0100101011100101
Notice that 11100101 is the low 8 bits of 0100101011100101.

## Slide 46: Jargon: Cache Conflict
Suppose that the cache address 11100101 currently contains RAM address 0100101011100101.
But, we now need to load RAM address 1100101011100101, which maps to the same cache address as 0100101011100101.
This is called a cache conflict : the CPU needs a RAM location that maps to a cache line already in use.
In the case of direct mapped cache, every cache conflict leads to the new cache line clobbering the old cache line.
This can lead to serious performance problems.
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 47: Problem with Direct Mapped: F90
If you have two arrays that start in the same place relative to cache, then they might clobber each other all the time: no cache hits!
REAL,DIMENSION(multiple_of_cache_size) :: a, b, c
INTEGER :: index
DO index = 1, multiple_of_cache_size
a(index) = b(index) + c(index)
END DO
In this example, a(index), b(index) and c(index) all map to the same cache line, so loading c(index) clobbers b(index) – no cache reuse!
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 48: Problem with Direct Mapped: C
If you have two arrays that start in the same place relative to cache, then they might clobber each other all the time: no cache hits!
float a[multiple_of_cache_size],
b[multiple_of_cache_size,
c[multiple_of_cache_size];
int index;
for (index = 0; index < multiple_of_cache_size;
index++)
{ a[index] = b[index] + c[index]; }
In this example, a[index], b[index] and c[index] all map to the same cache line, so loading c[index] clobbers b[index] – no cache reuse!
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 49: Fully Associative Cache
Fully Associative Cache can put any line of main memory into any cache line.
Typically, the cache management system will put the newly loaded data into the Least Recently Used cache line, though other strategies are possible (e.g., Random, First In First Out, Round Robin, Least Recently Modified).
So, this can solve, or at least reduce, the cache conflict problem.
But, fully associative cache tends to be expensive, so it’s pretty rare: you need Ncache. NRAM connections!
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 50: Fully Associative Illustration
Could go into
any cache line
Main Memory Address
0100101011100101

## Slide 51: Set Associative Cache
Set Associative Cache is a compromise between direct mapped and fully associative. A line in main memory can map to any of a fixed number of cache lines.
For example, 2-way Set Associative Cache can map each main memory line to either of 2 cache lines (e.g., to the Least Recently Used), 3-way maps to any of 3 cache lines, 4-way to 4 lines, and so on.
Set Associative cache is cheaper than fully associative – you need K . NRAM connections – but more robust than direct mapped.
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 52: 2-Way Set Associative Illustration
Could go into cache address
11100101
Main Memory Address
0100101011100101
Could go into
cache address
01100101
OR

## Slide 53: Cache Associativity Examples
Sandy Bridge [29]
  L1 data cache: 8-way set associative
  L2 cache: 8-way set associative
  L3 cache: varies with cache size
POWER4 [12]
  L1 instruction cache: direct mapped
  L1 data cache: 2-way set associative
  L2 cache: 8-way set associative
  L3 cache: 8-way set associative
POWER7 [28]
  L1 instruction cache: 4-way set associative
  L1 data cache: 8-way set associative
  L2 cache: 8-way set associative
  L3 cache: 8-way set associative
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 54: If It’s in Cache, It’s Also in RAM
As we saw earlier:
If a particular memory address is currently in cache, then it’s also in Main Memory (RAM).
That is, all of a program’s data are in Main Memory, but some are also in cache.
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 55: Changing a Value That’s in Cache
Suppose that you have in cache a particular line of main memory (RAM).
If you don’t change the contents of any of that line’s bytes while it’s in cache, then when it gets clobbered by another main memory line coming into cache, there’s no loss of information.
But, if you change the contents of any byte while it’s in cache, then you need to store it back out to main memory before clobbering it.
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 56: Cache Store Strategies
Typically, there are two possible cache store strategies:
Write-through: every single time that a value in cache is changed, that value is also stored back into main memory (RAM).
Write-back: every single time that a value in cache is changed, the cache line containing that cache location gets marked as dirty. When a cache line gets clobbered, then if it has been marked as dirty, then it is stored back into main memory (RAM). [14]
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 57: Cache Store Examples
Intel Sandy Bridge [29]
  L1 cache: write-back
Pentium D [26]
  L1 cache: write-through
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 58: The Importance of Being Local
[15]

## Slide 59: More Data Than Cache
Let’s say that you have 1000 times more data than cache. Then won’t most of your data be outside the cache?
YES!
Okay, so how does cache help?
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 60: Improving Your Cache Hit Rate
Many scientific codes use a lot more data than can fit in cache all at once.
Therefore, you need to ensure a high cache hit rate even though you’ve got much more data than cache.
So, how can you improve your cache hit rate?
Use the same solution as in Real Estate:
Location, Location, Location!
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 61: Data Locality
Data locality is the principle that, if you use data in a particular memory address, then very soon you’ll use either the same address or a nearby address.
Temporal locality: if you’re using address A now, then you’ll probably soon use address A again.
Spatial locality: if you’re using address A now, then you’ll probably soon use addresses between A-k and A+k, where k is small.
Note that this principle works well for sufficiently small values of “soon.”
Cache is designed to exploit locality, which is why a cache miss causes a whole line to be loaded.
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 62: Data Locality Is Empirical: C
Data locality has been observed empirically in many, many programs.
void ordered_fill (float* array, int array_length)
{ /* ordered_fill */
int index;
for (index = 0; index < array_length; index++) {
array[index] = index;
} /* for index */
} /* ordered_fill */
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 63: Data Locality Is Empirical: F90
Data locality has been observed empirically in many, many programs.
SUBROUTINE ordered_fill (array, array_length)
IMPLICIT NONE
INTEGER,INTENT(IN) :: array_length
REAL,DIMENSION(array_length),INTENT(OUT) :: array
INTEGER :: index
DO index = 1, array_length
array(index) = index
END DO
END SUBROUTINE ordered_fill
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 64: No Locality Example: C
In principle, you could write a program that exhibited absolutely no data locality at all:
void random_fill (float* array,
int* random_permutation_index,
int array_length)
{ /* random_fill */
int index;
for (index = 0; index < array_length; index++) {
array[random_permutation_index[index]] = index;
} /* for index */
} /* random_fill */
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 65: No Locality Example: F90
In principle, you could write a program that exhibited absolutely no data locality at all:
SUBROUTINE random_fill (array,
random_permutation_index, array_length)
IMPLICIT NONE
INTEGER,INTENT(IN) :: array_length
INTEGER,DIMENSION(array_length),INTENT(IN) :: &
& random_permutation_index
REAL,DIMENSION(array_length),INTENT(OUT) :: array
INTEGER :: index
DO index = 1, array_length
array(random_permutation_index(index)) = index
END DO
END SUBROUTINE random_fill
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 66: Permuted vs. Ordered
In a simple array fill, locality provides a factor of 8 to 20 speedup over a randomly ordered fill on a Pentium4.
Better

## Slide 67: Exploiting Data Locality
If you know that your code is capable of operating with a decent amount of data locality, then you can get speedup by focusing your energy on improving the locality of the code’s behavior.
This will substantially increase your cache reuse.
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 68: A Sample Application
Matrix-Matrix Multiply
Let A, B and C be matrices of sizes
nr  nc, nr  nk and nk  nc, respectively:
The definition of A = B • C is
for r  {1, nr}, c  {1, nc}.
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 69: Matrix Multiply w/Initialization
SUBROUTINE matrix_matrix_mult_by_init (dst, src1, src2, &
& nr, nc, nq)
IMPLICIT NONE
INTEGER,INTENT(IN) :: nr, nc, nq
REAL,DIMENSION(nr,nc),INTENT(OUT) :: dst
REAL,DIMENSION(nr,nq),INTENT(IN) :: src1
REAL,DIMENSION(nq,nc),INTENT(IN) :: src2
INTEGER :: r, c, q
DO c = 1, nc
DO r = 1, nr
dst(r,c) = 0.0
DO q = 1, nq
dst(r,c) = dst(r,c) + src1(r,q) * src2(q,c)
END DO !! q
END DO !! r
END DO !! c
END SUBROUTINE matrix_matrix_mult_by_init
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 70: Matrix Multiply w/Initialization
void matrix_matrix_mult_by_init (
float** dst, float** src1, float** src2,
int nr, int nc, int nq)
{ /* matrix_matrix_mult_by_init */
int r, c, q;
for (r = 0; r < nr; r++) {
for (c = 0; c < nc; c++) {
dst[r][c] = 0.0;
for (q = 0; q < nq; q++) {
dst[r][c] = dst[r][c] + src1[r][q] * src2[q][c];
} /* for q */
} /* for c */
} /* for r */
} /* matrix_matrix_mult_by_init */
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 71: Matrix Multiply Via Intrinsic
SUBROUTINE matrix_matrix_mult_by_intrinsic ( &
& dst, src1, src2, nr, nc, nq)
IMPLICIT NONE
INTEGER,INTENT(IN) :: nr, nc, nq
REAL,DIMENSION(nr,nc),INTENT(OUT) :: dst
REAL,DIMENSION(nr,nq),INTENT(IN) :: src1
REAL,DIMENSION(nq,nc),INTENT(IN) :: src2
dst = MATMUL(src1, src2)
END SUBROUTINE matrix_matrix_mult_by_intrinsic
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 72: Matrix Multiply Behavior
If the matrix is big, then each sweep of a row will clobber nearby values in cache.

## Slide 73: Performance of Matrix Multiply
Better

## Slide 74: Tiling

## Slide 75: Tiling
Tile: a small rectangular subdomain of a problem domain. Sometimes called a block or a chunk.
Tiling: breaking the domain into tiles.
Tiling strategy: operate on each tile to completion, then move to the next tile.
Tile size can be set at runtime, according to what’s best for the machine that you’re running on.
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 76: Tiling Code: F90
SUBROUTINE matrix_matrix_mult_by_tiling (dst, src1, src2, nr, nc, nq, &
& rtilesize, ctilesize, qtilesize)
IMPLICIT NONE
INTEGER,INTENT(IN) :: nr, nc, nq
REAL,DIMENSION(nr,nc),INTENT(OUT) :: dst
REAL,DIMENSION(nr,nq),INTENT(IN) :: src1
REAL,DIMENSION(nq,nc),INTENT(IN) :: src2
INTEGER,INTENT(IN) :: rtilesize, ctilesize, qtilesize
INTEGER :: rstart, rend, cstart, cend, qstart, qend
DO cstart = 1, nc, ctilesize
cend = cstart + ctilesize - 1
IF (cend > nc) cend = nc
DO rstart = 1, nr, rtilesize
rend = rstart + rtilesize - 1
IF (rend > nr) rend = nr
DO qstart = 1, nq, qtilesize
qend = qstart + qtilesize - 1
IF (qend > nq) qend = nq
CALL matrix_matrix_mult_tile(dst, src1, src2, nr, nc, nq, &
& rstart, rend, cstart, cend, qstart, qend)
END DO !! qstart
END DO !! rstart
END DO !! cstart
END SUBROUTINE matrix_matrix_mult_by_tiling
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 77: Tiling Code: C
void matrix_matrix_mult_by_tiling (
float** dst, float** src1, float** src2,
int nr, int nc, int nq,
int rtilesize, int ctilesize, int qtilesize)
{ /* matrix_matrix_mult_by_tiling */
int rstart, rend, cstart, cend, qstart, qend;
for (rstart = 0; rstart < nr; rstart += rtilesize) {
rend = rstart + rtilesize – 1;
if (rend >= nr) rend = nr - 1;
for (cstart = 0; cstart < nc; cstart += ctilesize) {
cend = cstart + ctilesize – 1;
if (cend >= nc) cend = nc - 1;
for (qstart = 0; qstart < nq; qstart += qtilesize) {
qend = qstart + qtilesize – 1;
if (qend >= nq) qend = nq - 1;
matrix_matrix_mult_tile(dst, src1, src2, nr, nc, nq,
rstart, rend, cstart, cend, qstart, qend);
} /* for qstart */
} /* for cstart */
} /* for rstart */
} /* matrix_matrix_mult_by_tiling */
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 78: Multiplying Within a Tile: F90
SUBROUTINE matrix_matrix_mult_tile (dst, src1, src2, nr, nc, nq, &
& rstart, rend, cstart, cend, qstart, qend)
IMPLICIT NONE
INTEGER,INTENT(IN) :: nr, nc, nq
REAL,DIMENSION(nr,nc),INTENT(OUT) :: dst
REAL,DIMENSION(nr,nq),INTENT(IN) :: src1
REAL,DIMENSION(nq,nc),INTENT(IN) :: src2
INTEGER,INTENT(IN) :: rstart, rend, cstart, cend, qstart, qend
INTEGER :: r, c, q
DO c = cstart, cend
DO r = rstart, rend
IF (qstart == 1) dst(r,c) = 0.0
DO q = qstart, qend
dst(r,c) = dst(r,c) + src1(r,q) * src2(q,c)
END DO !! q
END DO !! r
END DO !! c
END SUBROUTINE matrix_matrix_mult_tile
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 79: Multiplying Within a Tile: C
void matrix_matrix_mult_tile (
float** dst, float** src1, float** src2,
int nr, int nc, int nq,
int rstart, int rend, int cstart, int cend,
int qstart, int qend)
{ /* matrix_matrix_mult_tile */
int r, c, q;
for (r = rstart; r <= rend; r++) {
for (c = cstart; c <= cend; c++) {
if (qstart == 0) dst[r][c] = 0.0;
for (q = qstart; q <= qend; q++) {
dst[r][c] = dst[r][c] + src1[r][q] * src2[q][c];
} /* for q */
} /* for c */
} /* for r */
} /* matrix_matrix_mult_tile */
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 80: Performance with Tiling
Better

## Slide 81: The Advantages of Tiling
It allows your code to exploit data locality better, to get much more cache reuse: your code runs faster!
It’s a relatively modest amount of extra coding (typically a few wrapper functions and some changes to loop bounds).
If you don’t need tiling – because of the hardware, the compiler or the problem size – then you can turn it off by simply setting the tile size equal to the problem size.
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 82: Will Tiling Always Work?
Tiling WON’T always work. Why?
Well, tiling works well when:
the order in which calculations occur doesn’t matter much, AND
there are lots and lots of calculations to do for each memory movement.
If either condition is absent, then tiling won’t help.
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 83: Hard Disk

## Slide 84: Why Is Hard Disk Slow?
Your hard disk is much much slower than main memory (factor of 10-1000). Why?
Well, accessing data on the hard disk involves physically moving:
  the disk platter
  the read/write head
In other words, hard disk is slow because objects move much slower than electrons: Newtonian speeds are much slower than Einsteinian speeds.
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 85: I/O Strategies
Read and write the absolute minimum amount.
Don’t reread the same data if you can keep it in memory.
Write binary instead of characters.
Use optimized I/O libraries like NetCDF [17] and HDF [18].
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 86: Avoid Redundant I/O: C
An actual piece of code seen at OU:
for (thing = 0; thing < number_of_things; thing++) {
for (timestep = 0; timestep < number_of_timesteps; timestep++) {
read_file(filename[timestep]);
do_stuff(thing, timestep);
} /* for timestep */
} /* for thing */
Improved version:
for (timestep = 0; timestep < number_of_timesteps; timestep++) {
read_file(filename[timestep]);
for (thing = 0; thing < number_of_things; thing++) {
do_stuff(thing, timestep);
} /* for thing */
} /* for timestep */
Savings (in real life): factor of 500!
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 87: Avoid Redundant I/O: F90
An actual piece of code seen at OU:
DO thing = 1, number_of_things
DO timestep = 1, number_of_timesteps
CALL read_file(filename(timestep))
CALL do_stuff(thing, timestep)
END DO !! timestep
END DO !! thing
Improved version:
DO timestep = 1, number_of_timesteps
CALL read_file(filename(timestep))
DO thing = 1, number_of_things
CALL do_stuff(thing, timestep)
END DO !! thing
END DO !! timestep
Savings (in real life): factor of 500!
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 88: Write Binary, Not ASCII
When you write binary data to a file, you’re writing (typically) 4 bytes per value.
When you write ASCII (character) data, you’re writing (typically) 8-16 bytes per value.
So binary saves a factor of 2 to 4 (typically).
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 89: Problem with Binary I/O
There are many ways to represent data inside a computer, especially floating point (real) data.
Often, the way that one kind of computer (e.g., an Intel i7) saves binary data is different from another kind of computer (e.g., an IBM POWER7).
So, a file written on an Intel i7 machine may not be readable on an IBM POWER7.
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 90: Portable I/O Libraries
NetCDF and HDF are the two most commonly used I/O libraries for scientific computing.
Each has its own internal way of representing numerical data. When you write a file using, say, HDF, it can be read by a HDF on any kind of computer.
Plus, these libraries are optimized to make the I/O very fast.
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 91: Virtual Memory

## Slide 92: Virtual Memory
Typically, the amount of main memory (RAM) that a CPU can address is larger than the amount of data physically present in the computer.
For example, consider a laptop that can address 1 TB of main memory (roughly 1 trillion bytes), but only contains 4 GB (roughly 4 billion bytes).
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 93: Virtual Memory (cont’d)
Locality: Most programs don’t jump all over the memory that they use; instead, they work in a particular area of memory for a while, then move to another area.
So, you can offload onto hard disk much of the memory image of a program that’s running.
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 94: Virtual Memory (cont’d)
Memory is chopped up into many pages of modest size (e.g., 1 KB – 32 KB; typically 4 KB).
Only pages that have been recently used actually reside in memory; the rest are stored on hard disk.
Hard disk is 10 to 1,000 times slower than main memory, so you get better performance if you rarely get a page fault, which forces a read from (and maybe a write to) hard disk: exploit data locality!
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 95: Cache vs. Virtual Memory
Lines (cache) vs. pages (VM)
Cache faster than RAM (cache) vs. RAM faster than disk (VM)
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 96: Storage Use Strategies
Register reuse: do a lot of work on the same data before working on new data.
Cache reuse: the program is much more efficient if all of the data and instructions fit in cache; if not, try to use what’s in cache a lot before using anything that isn’t in cache (e.g., tiling).
Data locality: try to access data that are near each other in memory before data that are far.
I/O efficiency: do a bunch of I/O all at once rather than a little bit at a time; don’t mix calculations and I/O.
Supercomputing in Plain English: Storage Hierarchy
Tue Jan 29 2013

## Slide 97: OK Supercomputing Symposium 2013
2006 Keynote:
Dan Atkins
Head of NSF’s
Office of
Cyberinfrastructure
2004 Keynote:
Sangtae Kim
NSF Shared
Cyberinfrastructure
Division Director
2003 Keynote:
Peter Freeman
NSF
Computer & Information
Science & Engineering
Assistant Director
2005 Keynote:
Walt Brooks
NASA Advanced
Supercomputing
Division Director
2007 Keynote:
Jay Boisseau
Director
Texas Advanced
Computing Center
U. Texas Austin
2008 Keynote: José Munoz Deputy Office Director/ Senior Scientific Advisor NSF Office of Cyberinfrastructure
2009 Keynote: Douglass Post Chief Scientist US Dept of Defense HPC Modernization Program
FREE! Wed Oct 2 2013 @ OU
Over 235 registra2ons already!
Over 150 in the first day, over 200 in the first week, over 225 in the first month.
http://symposium2013.oscer.ou.edu/
Reception/Poster Session
Tue Oct 1 2013 @ OU
Symposium Wed Oct 2 2013 @ OU
2010 Keynote: Horst Simon Deputy Director Lawrence Berkeley National Laboratory
2013 Keynote to be announced!
2011 Keynote: Barry Schneider Program Manager National Science Foundation
2012 Keynote: Thom Dunning Director National Center for Supercomputing Applications

## Slide 98: Thanks for your attention! Questions? www.oscer.ou.edu

## Slide 99: References
[1] http://graphics8.nytimes.com/images/2007/07/13/sports/auto600.gif
[2] http://www.vw.com/newbeetle/
[3] http://img.dell.com/images/global/products/resultgrid/sm/latit_d630.jpg
[4] http://en.wikipedia.org/wiki/X64
[5] Richard Gerber, The Software Optimization Cookbook: High-performance Recipes for the Intel Architecture. Intel Press, 2002, pp. 161-168.
[6] http://www.anandtech.com/showdoc.html?i=1460&p=2
[8] http://www.toshiba.com/taecdpd/products/features/MK2018gas-Over.shtml
[9] http://www.toshiba.com/taecdpd/techdocs/sdr2002/2002spec.shtml
[10] ftp://download.intel.com/design/Pentium4/manuals/24896606.pdf
[11] http://www.pricewatch.com/
[12] http://en.wikipedia.org/wiki/POWER7
[13] http://www.kingston.com/branded/image_files/nav_image_desktop.gif
14] M. Wolfe, High Performance Compilers for Parallel Computing. Addison-Wesley Publishing Company, Redwood City CA, 1996.
[15] http://www.visit.ou.edu/vc_campus_map.htm
[16] http://www.storagereview.com/
[17] http://www.unidata.ucar.edu/packages/netcdf/
[18] http://hdf.ncsa.uiuc.edu/
[23] http://en.wikipedia.org/wiki/Itanium
[19] ftp://download.intel.com/design/itanium2/manuals/25111003.pdf
[20] http://images.tomshardware.com/2007/08/08/extreme_fsb_2/qx6850.jpg (em64t)
[21] http://www.pcdo.com/images/pcdo/20031021231900.jpg (power5)
[22] http://vnuuk.typepad.com/photos/uncategorized/itanium2.jpg (i2)
[??] http://www.anandtech.com/cpuchipsets/showdoc.aspx?i=2353&p=2 (Prescott cache latency)
[??] http://www.xbitlabs.com/articles/mobile/print/core2duo.html (T2400 Merom cache)
[??] http://www.lenovo.hu/kszf/adatlap/Prosi_Proc_Core2_Mobile.pdf (Merom cache line size)
[25] http://www.lithium.it/nove3.jpg
[26] http://cpu.rightmark.org/
[27] Tribuvan Kumar Prakash, “Performance Analysis of Intel Core 2 Duo Processor.” MS Thesis, Dept of Electrical and Computer Engineering, Louisiana State University, 2007.
[28] R. Kalla, IBM, personal communication, 10/26/2010.
[29] Intel® 64 and IA-32 Architectures Optimization Reference Manual
http://www.intel.com/Assets/en_US/PDF/manual/248966.pdf